## Slide 1: Comp Sci 310
Day 25

## Slide 2: Announcements
Quiz 10 on Friday, 10/31
  MULTIcycle architecture
    Datapath, control unit
    Example: Implement a new operation on top of existing functionality
Quiz 11 on Monday, 11/3
  A different multiplication algorithm
Exam 2 on Friday, 11/7
Assignment 4 posted tonight
  SINGLEcycle implementation

## Slide 3: A special announcement
CS 480 and 391 have low enrollments
Take these courses!

## Slide 4: Larc FSM: implementation (next state logic)
FSM
Next state comb. logic
Output comb. logic
State register
4
5
5
23

## Slide 5: MULTIcycle Larc CU FSM (with transitions)
IR  M[PC]
PC  PC + 1
RD1  Reg[RB]
RD2  Reg[RC]
ALUout  PC + SE(LIMM)
ALUout  RD1 + RD2
ALUout  RD1 - RD2
ALUout  RD1 Nor RD2
ALUout  ( RD1 < RD2 ? 1 : 0 )
Reg[RA]  SE(LIMM)
Reg[RA]  LIMM << 8
PC  ( RD2 - 0 == 0 ? ALUout : PC )
ALUout  RD1 + SE(SIMM)
ALUout  RD1 + SE(SIMM)
Reg[RA]  PC
PC  RD1
PC  ( RD2 - 0 != 0 ? ALUout : PC )
MDR  M[ALUout]
Reg[RA]  MDR
M[ALUout]  RD2
Memory
Fetch
Write
Execute
Decode
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Reg[RA]  ALUout
Op=0000
Op=0001
Op=0110
Op=0111
Op=1000
Op=1001
Op=1010
Op=1011
Op=1100
Op=1101
Op=1110

## Slide 6: MULTIcycle Larc CU FSM (with transitions)
IR  M[PC]
PC  PC + 1
RD1  Reg[RB]
RD2  Reg[RC]
ALUout  PC + SE(LIMM)
ALUout  RD1 + RD2
ALUout  RD1 - RD2
ALUout  RD1 Nor RD2
ALUout  ( RD1 < RD2 ? 1 : 0 )
Reg[RA]  SE(LIMM)
Reg[RA]  LIMM << 8
PC  ( RD2 - 0 == 0 ? ALUout : PC )
ALUout  RD1 + SE(SIMM)
ALUout  RD1 + SE(SIMM)
Reg[RA]  PC
PC  RD1
PC  ( RD2 - 0 != 0 ? ALUout : PC )
MDR  M[ALUout]
Reg[RA]  MDR
M[ALUout]  RD2
Memory
Fetch
Write
Execute
Decode
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Reg[RA]  ALUout
Op=0000
Op=0001
Op=0110
Op=0111
Op=1000
Op=1001
Op=1010
Op=1011
Op=1100
Op=1101
Op=1110
Current state | Next state | Opcode

## Slide 7: MULTIcycle Larc CU FSM (with transitions)
IR  M[PC]
PC  PC + 1
RD1  Reg[RB]
RD2  Reg[RC]
ALUout  PC + SE(LIMM)
ALUout  RD1 + RD2
ALUout  RD1 - RD2
ALUout  RD1 Nor RD2
ALUout  ( RD1 < RD2 ? 1 : 0 )
Reg[RA]  SE(LIMM)
Reg[RA]  LIMM << 8
PC  ( RD2 - 0 == 0 ? ALUout : PC )
ALUout  RD1 + SE(SIMM)
ALUout  RD1 + SE(SIMM)
Reg[RA]  PC
PC  RD1
PC  ( RD2 - 0 != 0 ? ALUout : PC )
MDR  M[ALUout]
Reg[RA]  MDR
M[ALUout]  RD2
Memory
Fetch
Write
Execute
Decode
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Reg[RA]  ALUout
Op=0000
Op=0001
Op=0110
Op=0111
Op=1000
Op=1001
Op=1010
Op=1011
Op=1100
Op=1101
Op=1110
Current state | Next state | Opcode
 | 0 | 
 | 1 | 
 | 2 | 
 | 3 | 
 | 4 | 
 | 5 | 
 | 6 | 
 | 7 | 
 | 8 | 
 | 9 | 
 | 10 | 
 | 11 | 
 | 12 | 
 | 13 | 
 | 14 | 
 | 15 | 
 | 16 | 

## Slide 8: MULTIcycle Larc CU FSM (with transitions)
IR  M[PC]
PC  PC + 1
RD1  Reg[RB]
RD2  Reg[RC]
ALUout  PC + SE(LIMM)
ALUout  RD1 + RD2
ALUout  RD1 - RD2
ALUout  RD1 Nor RD2
ALUout  ( RD1 < RD2 ? 1 : 0 )
Reg[RA]  SE(LIMM)
Reg[RA]  LIMM << 8
PC  ( RD2 - 0 == 0 ? ALUout : PC )
ALUout  RD1 + SE(SIMM)
ALUout  RD1 + SE(SIMM)
Reg[RA]  PC
PC  RD1
PC  ( RD2 - 0 != 0 ? ALUout : PC )
MDR  M[ALUout]
Reg[RA]  MDR
M[ALUout]  RD2
Memory
Fetch
Write
Execute
Decode
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Reg[RA]  ALUout
Op=0000
Op=0001
Op=0110
Op=0111
Op=1000
Op=1001
Op=1010
Op=1011
Op=1100
Op=1101
Op=1110
Current state | Next state | Opcode
3, 7, 8, 9, 10, 13, 15, 16 | 0 | 
0 | 1 | 
1 | 2 | 
2, 4, 5, 6 | 3 | 
1 | 4 | 
1 | 5 | 
1 | 6 | 
1 | 7 | 
1 | 8 | 
1 | 9 | 
1 | 10 | 
1 | 11 | 
11 | 12 | 
12 | 13 | 
1 | 14 | 
14 | 15 | 
1 | 16 | 

## Slide 9: MULTIcycle Larc CU FSM (with transitions)
IR  M[PC]
PC  PC + 1
RD1  Reg[RB]
RD2  Reg[RC]
ALUout  PC + SE(LIMM)
ALUout  RD1 + RD2
ALUout  RD1 - RD2
ALUout  RD1 Nor RD2
ALUout  ( RD1 < RD2 ? 1 : 0 )
Reg[RA]  SE(LIMM)
Reg[RA]  LIMM << 8
PC  ( RD2 - 0 == 0 ? ALUout : PC )
ALUout  RD1 + SE(SIMM)
ALUout  RD1 + SE(SIMM)
Reg[RA]  PC
PC  RD1
PC  ( RD2 - 0 != 0 ? ALUout : PC )
MDR  M[ALUout]
Reg[RA]  MDR
M[ALUout]  RD2
Memory
Fetch
Write
Execute
Decode
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Reg[RA]  ALUout
Op=0000
Op=0001
Op=0110
Op=0111
Op=1000
Op=1001
Op=1010
Op=1011
Op=1100
Op=1101
Op=1110
Current state | Next state | Opcode
3, 7, 8, 9, 10, 13, 15, 16 | 0 | 
0 | 1 | 
1 | 2 | 0000 add
2, 4, 5, 6 | 3 | 
1 | 4 | 0001 sub
1 | 5 | 0110 nor
1 | 6 | 0111 slt
1 | 7 | 1000 li
1 | 8 | 1001 lui
1 | 9 | 1010 beq
1 | 10 | 1011 bne
1 | 11 | 1100 lw
11 | 12 | 
12 | 13 | 
1 | 14 | 1101 sw
14 | 15 | 
1 | 16 | 1110 jalr

## Slide 10: Implementation of next state logic
Current state | Next state | Opcode
3, 7, 8, 9, 10, 13, 15, 16 | 0 | 
0 | 1 | 
1 | 2 | 0000 add
2, 4, 5, 6 | 3 | 
1 | 4 | 0001 sub
1 | 5 | 0110 nor
1 | 6 | 0111 slt
1 | 7 | 1000 li
1 | 8 | 1001 lui
1 | 9 | 1010 beq
1 | 10 | 1011 bne
1 | 11 | 1100 lw
11 | 12 | 
12 | 13 | 
1 | 14 | 1101 sw
14 | 15 | 
1 | 16 | 1110 jalr
How to turn this into a circuit?

## Slide 11: State encoding
Each state can be encoded as a binary number
  Take the binary representation of the state number
    See the FSM for the CU
For example, state6 is encoded as 00110
  Or: S4 = 0, S3 = 0, S2 = 1, S1 = 1, S0 = 0
    These are the “current state” signals

## Slide 12: Implementation of next state logic
Current state | Next state |  | Opcode
3, 7, 8, 9, 10, 13, 15, 16 | 00000 | 0 | 
0 | 00001 | 1 | 
1 | 00010 | 2 | 0000 add
2, 4, 5, 6 | 00011 | 3 | 
1 | 00100 | 4 | 0001 sub
1 | 00101 | 5 | 0110 nor
1 | 00110 | 6 | 0111 slt
1 | 00111 | 7 | 1000 li
1 | 01000 | 8 | 1001 lui
1 | 01001 | 9 | 1010 beq
1 | 01010 | 10 | 1011 bne
1 | 01011 | 11 | 1100 lw
11 | 01100 | 12 | 
12 | 01101 | 13 | 
1 | 01110 | 14 | 1101 sw
14 | 01111 | 15 | 
1 | 10000 | 16 | 1110 jalr

## Slide 13: Two observations
We can write state6 as: ¬S4 Λ ¬S3 Λ S2 Λ S1 Λ ¬S0
  This logic equation is true if and only if “state6 is the current state”
    Equations corresponding to other states would all be false
      Why?
We can do the same kind of thing for opcodes:
  E.g., NOR = 0110 = ¬OP3 Λ OP2 Λ OP1 Λ ¬OP0
    This logic equation is true if and only if “NOR is the current opcode”

## Slide 14: Larc FSM: implementation (next state logic)
FSM
Next state comb. logic
Output comb. logic
State register
4
5
5
23
Next state comb. logic
Op0
Op1
Op2
Op3
S0
S1
S2
S3
S4
Ns0
Ns1
Ns2
Ns3
Ns4
State register

## Slide 15: Logic equations
We just need to get logic equations for Ns0, … Ns4
  In terms of Op0, … Op3 and S0, …, S4.
How do we get these?

## Slide 16: NS0
The next-state bit NS0 should be active whenever the next state has NS0 = 1 in the state encoding
For which (current) states is this true?

## Slide 17: Implementation of next state logic
Current state | Next state |  | Opcode
3, 7, 8, 9, 10, 13, 15, 16 | 00000 | 0 | 
0 | 00001 | 1 | 
1 | 00010 | 2 | 0000 add
2, 4, 5, 6 | 00011 | 3 | 
1 | 00100 | 4 | 0001 sub
1 | 00101 | 5 | 0110 nor
1 | 00110 | 6 | 0111 slt
1 | 00111 | 7 | 1000 li
1 | 01000 | 8 | 1001 lui
1 | 01001 | 9 | 1010 beq
1 | 01010 | 10 | 1011 bne
1 | 01011 | 11 | 1100 lw
11 | 01100 | 12 | 
12 | 01101 | 13 | 
1 | 01110 | 14 | 1101 sw
14 | 01111 | 15 | 
1 | 10000 | 16 | 1110 jalr
Look at the “Current state” column…
For which current states is NS0 = 1?

## Slide 18: Implementation of next state logic
Current state | Next state |  | Opcode
3, 7, 8, 9, 10, 13, 15, 16 | 00000 | 0 | 
0 | 00001 | 1 | 
1 | 00010 | 2 | 0000 add
2, 4, 5, 6 | 00011 | 3 | 
1 | 00100 | 4 | 0001 sub
1 | 00101 | 5 | 0110 nor
1 | 00110 | 6 | 0111 slt
1 | 00111 | 7 | 1000 li
1 | 01000 | 8 | 1001 lui
1 | 01001 | 9 | 1010 beq
1 | 01010 | 10 | 1011 bne
1 | 01011 | 11 | 1100 lw
11 | 01100 | 12 | 
12 | 01101 | 13 | 
1 | 01110 | 14 | 1101 sw
14 | 01111 | 15 | 
1 | 10000 | 16 | 1110 jalr
Look at the “Current state” column…
For which current states is NS0 = 1?

## Slide 19: NS0 (continued)
The next-state bit NS0 should be active whenever the next state has NS0 = 1 in the state encoding
For which (current) states is this true?
0
2
4
5
6
1 (and NOR opcode)
1 (and LI opcode)
1 (and BEQ opcode)
1 (and LW opcode)
12
14

## Slide 20: NS0 (continued)
The next-state bit NS0 should be active whenever the next state has NS0 = 1 in the state encoding
For which (current) states is this true?
0 = State0 = ¬S4 Λ ¬S3 Λ ¬S2 Λ ¬S1 Λ ¬S0
2 = State2 = ¬S4 Λ ¬S3 Λ ¬S2 Λ S1 Λ ¬S0
4 = State4 = ¬S4 Λ ¬S3 Λ S2 Λ ¬S1 Λ ¬S0
5 = State5 = ¬S4 Λ ¬S3 Λ S2 Λ ¬S1 Λ S0
6 = State6 = ¬S4 Λ ¬S3 Λ S2 Λ S1 Λ ¬S0
1 (and NOR opcode) =
1 (and LI opcode)
1 (and BEQ opcode)
1 (and LW opcode)
12 = State12 = ¬S4 Λ S3 Λ S2 Λ ¬S1 Λ ¬S0
14 = State14 = ¬S4 Λ S3 Λ S2 Λ S1 Λ ¬S0

## Slide 21: NS0 (continued)
The next-state bit NS0 should be active whenever the next state has NS0 = 1 in the state encoding
For which (current) states is this true?
0 = State0 = ¬S4 Λ ¬S3 Λ ¬S2 Λ ¬S1 Λ ¬S0
2 = State2 = ¬S4 Λ ¬S3 Λ ¬S2 Λ S1 Λ ¬S0
4 = State4 = ¬S4 Λ ¬S3 Λ S2 Λ ¬S1 Λ ¬S0
5 = State5 = ¬S4 Λ ¬S3 Λ S2 Λ ¬S1 Λ S0
6 = State6 = ¬S4 Λ ¬S3 Λ S2 Λ S1 Λ ¬S0
1 (and NOR opcode) = ???
1 (and LI opcode)
1 (and BEQ opcode)
1 (and LW opcode)
12 = State12 = ¬S4 Λ S3 Λ S2 Λ ¬S1 Λ ¬S0
14 = State14 = ¬S4 Λ S3 Λ S2 Λ S1 Λ ¬S0

## Slide 22: NS0 (continued)
The next-state bit NS0 should be active whenever the next state has NS0 = 1 in the state encoding
For which (current) states is this true?
0 = State0 = ¬S4 Λ ¬S3 Λ ¬S2 Λ ¬S1 Λ ¬S0
2 = State2 = ¬S4 Λ ¬S3 Λ ¬S2 Λ S1 Λ ¬S0
4 = State4 = ¬S4 Λ ¬S3 Λ S2 Λ ¬S1 Λ ¬S0
5 = State5 = ¬S4 Λ ¬S3 Λ S2 Λ ¬S1 Λ S0
6 = State6 = ¬S4 Λ ¬S3 Λ S2 Λ S1 Λ ¬S0
1 (and NOR opcode) = State1 Λ NOR
1 (and LI opcode) = State1 Λ LI
1 (and BEQ opcode) = State1 Λ BEQ
1 (and LW opcode) = State1 Λ LW
12 = State12 = ¬S4 Λ S3 Λ S2 Λ ¬S1 Λ ¬S0
14 = State14 = ¬S4 Λ S3 Λ S2 Λ S1 Λ ¬S0

## Slide 23: NS0 (continued)
The next-state bit NS0 should be active whenever the next state has NS0 = 1 in the state encoding
For which (current) states is this true?
0 = State0 = ¬S4 Λ ¬S3 Λ ¬S2 Λ ¬S1 Λ ¬S0
2 = State2 = ¬S4 Λ ¬S3 Λ ¬S2 Λ S1 Λ ¬S0
4 = State4 = ¬S4 Λ ¬S3 Λ S2 Λ ¬S1 Λ ¬S0
5 = State5 = ¬S4 Λ ¬S3 Λ S2 Λ ¬S1 Λ S0
6 = State6 = ¬S4 Λ ¬S3 Λ S2 Λ S1 Λ ¬S0
1 (and NOR opcode) = State1 Λ NOR = ¬S4 Λ ¬S3 Λ ¬S2 Λ ¬S1 Λ S0 Λ NOR
1 (and LI opcode) = State1 Λ LI
1 (and BEQ opcode) = State1 Λ BEQ
1 (and LW opcode) = State1 Λ LW
12 = State12 = ¬S4 Λ S3 Λ S2 Λ ¬S1 Λ ¬S0
14 = State14 = ¬S4 Λ S3 Λ S2 Λ S1 Λ ¬S0

## Slide 24: NS0 (continued)
The next-state bit NS0 should be active whenever the next state has NS0 = 1 in the state encoding
For which (current) states is this true?
0 = State0 = ¬S4 Λ ¬S3 Λ ¬S2 Λ ¬S1 Λ ¬S0
2 = State2 = ¬S4 Λ ¬S3 Λ ¬S2 Λ S1 Λ ¬S0
4 = State4 = ¬S4 Λ ¬S3 Λ S2 Λ ¬S1 Λ ¬S0
5 = State5 = ¬S4 Λ ¬S3 Λ S2 Λ ¬S1 Λ S0
6 = State6 = ¬S4 Λ ¬S3 Λ S2 Λ S1 Λ ¬S0
1 (and NOR opcode) = State1 Λ NOR = ¬S4 Λ ¬S3 Λ ¬S2 Λ ¬S1 Λ S0
Λ ¬OP3 Λ OP2 Λ OP1 Λ ¬OP0
1 (and LI opcode) = State1 Λ LI
1 (and BEQ opcode) = State1 Λ BEQ
1 (and LW opcode) = State1 Λ LW
12 = State12 = ¬S4 Λ S3 Λ S2 Λ ¬S1 Λ ¬S0
14 = State14 = ¬S4 Λ S3 Λ S2 Λ S1 Λ ¬S0

## Slide 25: NS0 (continued)
NS0 = ( ¬S4 Λ ¬S3 Λ ¬S2 Λ ¬S1 Λ ¬S0 )
V ( ¬S4 Λ ¬S3 Λ ¬S2 Λ S1 Λ ¬S0 )
V ( ¬S4 Λ ¬S3 Λ S2 Λ ¬S1 Λ ¬S0 )
V ( ¬S4 Λ ¬S3 Λ S2 Λ ¬S1 Λ S0 )
V ( ¬S4 Λ ¬S3 Λ S2 Λ S1 Λ ¬S0 )
V ( ¬S4 Λ ¬S3 Λ ¬S2 Λ ¬S1 Λ S0
Λ ¬OP3 Λ OP2 Λ OP1 Λ ¬OP0 )
V (you do this one)
V (you do this one)
V (you do this one)
V ( ¬S4 Λ S3 Λ S2 Λ ¬S1 Λ ¬S0 )
V ( ¬S4 Λ S3 Λ S2 Λ S1 Λ ¬S0 )
Now just do this for NS1, NS2 and NS3, and you have the “next state outputs” of our FSM…

## Slide 26: Larc FSM: implementation (next state logic)
FSM
Next state comb. logic
Output comb. logic
State register
4
5
5
23
Next state comb. logic
Op0
Op1
Op2
Op3
S0
S1
S2
S3
S4
Ns0
Ns1
Ns2
Ns3
Ns4
State register

## Slide 27: Any questions?

## Slide 28: Example
Add a new instruction to the existing MULTIcycle Larc microarchitecture
  Only make “gentle” modifications
    Add wires, add/expand multiplexers, etc.
      Do not add new registers, ALUs, memories, etc.
Swap(Reg[Rb], Reg[Rc])
  The values stored in Reg[Rb] and Reg[Rc] are swapped

## Slide 29: MULTIcycle datapath implementation
PC
M
IR
MDR
RF
RD1
RD2
ALUOUT
SIGN EXTEND
SHL8
SIGN EXTEND
SIGN EXTEND
1
0
z
ALU
CONTROL UNIT
M Write
PC Write
M Src
IR write
MDR write
LI
LW
SorL
RD1 Write
RD2 Write
ALU2
ALU1
SUB
NOR
ALUout Write
BE
BN
BN
BE
JAL
RFWD
2
OPCODE[12..15]
LIMM[4..11]
SIMM[0..3]
SIMM[8..11]
LIMM
[0..7]
RA[8..11]
RC[0..3]
RB[4..7]
10
01
00
11
2
2
RF Write

## Slide 30: Swap stages
Fetch (same as before)
Decode (same as before)
Execute ???
Memory ???
Write ???

## Slide 31: Instruction encoding / semantics
Reg[Rb]  RD2
Reg[Rc]  RD1
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
Opcode
Src. Reg. #1
Rb
UNUSED
Rc
Src. Reg. #2
Notes: This doesn’t work

## Slide 32: MULTIcycle datapath implementation
PC
M
IR
MDR
RF
RD1
RD2
ALUOUT
SIGN EXTEND
SHL8
SIGN EXTEND
SIGN EXTEND
1
0
z
ALU
CONTROL UNIT
M Write
PC Write
M Src
IR write
MDR write
LI
LW
SorL
RD1 Write
RD2 Write
ALU2
ALU1
SUB
NOR
ALUout Write
BE
BN
BN
BE
JAL
RFWD
2
OPCODE[12..15]
LIMM[4..11]
SIMM[0..3]
SIMM[8..11]
LIMM
[0..7]
RA[8..11]
RC[0..3]
RB[4..7]
10
01
00
11
2
2
RF Write

## Slide 33: MULTIcycle SWAP
PC
M
IR
MDR
RF
RD1
RD2
ALUOUT
SIGN EXTEND
SHL8
SIGN EXTEND
SIGN EXTEND
1
0
z
ALU
CONTROL UNIT
M Write
PC Write
M Src
IR write
MDR write
SWAP
LW
SorL
RD1 Write
RD2 Write
ALU2
ALU1
SUB
NOR
ALUout Write
BE
BN
BN
BE
JAL
RFWD
2
OPCODE[12..15]
LIMM[4..11]
SIMM[0..3]
SIMM[8..11]
LIMM
[0..7]
RA[8..11]
RC[0..3]
RB[4..7]
10
01
00
11
2
2
RF Write
RD1
RD2
LI
Notes: This doesn’t work

## Slide 34: MULTIcycle SWAP
PC
M
IR
MDR
RF
RD1
RD2
ALUOUT
SIGN EXTEND
SHL8
SIGN EXTEND
SIGN EXTEND
1
0
z
ALU
CONTROL UNIT
M Write
PC Write
M Src
IR write
MDR write
SWAP
LW
SorL
RD1 Write
RD2 Write
ALU2
ALU1
SUB
NOR
ALUout Write
BE
BN
BN
BE
JAL
RFWD
3
OPCODE[12..15]
LIMM[4..11]
SIMM[0..3]
SIMM[8..11]
LIMM
[0..7]
RA[8..11]
RC[0..3]
RB[4..7]
10
01
00
11
2
2
RF Write
RD1
RD2
2
LI
Notes: This doesn’t work

## Slide 35: Control signal (before)
State | PC Write | M Src | M write | IR Write | MDR write | LW | LI | RFwd |  | RF Write | SorL | RD1 write | RD2 write | ALU1 |  | ALU2 |  | SUB | NOR | BN | BE | ALU out | JAL
0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 36: Control signal (after)
State | PC Write | M Src | M write | IR Write | MDR write | LW | LI | RFwd |  |  | RF Write | SorL | RD1 write | RD2 write | ALU1 |  | ALU2 |  | SUB | NOR | BN | BE | ALU out | JAL
0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 37: Control signal (after)
State | PC Write | M Src | M write | IR Write | MDR write | LW | LI | RFwd |  |  | RF Write | SorL | RD1 write | RD2 write | ALU1 |  | ALU2 |  | SUB | NOR | BN | BE | ALU out | JAL | Swap | 
0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 38: MULTIcycle SWAP control ???
IR  M[PC]
PC  PC + 1
RD1  Reg[RB]
RD2  Reg[RC]
ALUout  PC + SE(LIMM)
Reg[Rb]  RD2
Reg[Rc]  RD1
0
1
17
Op=????
Can’t do two RF writes in one step!

## Slide 39: MULTIcycle SWAP control
IR  M[PC]
PC  PC + 1
RD1  Reg[RB]
RD2  Reg[RC]
ALUout  PC + SE(LIMM)
Reg[Rb]  RD2
0
1
17
Op=????
Reg[Rc]  RD1
18

## Slide 40: MULTIcycle SWAP
PC
M
IR
MDR
RF
RD1
RD2
ALUOUT
SIGN EXTEND
SHL8
SIGN EXTEND
SIGN EXTEND
1
0
z
ALU
CONTROL UNIT
M Write
PC Write
M Src
IR write
MDR write
SWAP
LW
SorL
RD1 Write
RD2 Write
ALU2
ALU1
SUB
NOR
ALUout Write
BE
BN
BN
BE
JAL
RFWD
3
OPCODE[12..15]
LIMM[4..11]
SIMM[0..3]
SIMM[8..11]
LIMM
[0..7]
RA[8..11]
RC[0..3]
RB[4..7]
10
01
00
11
2
2
RF Write
RD1
RD2
2
LI
This might not work!
Notes: This doesn’t work unless RD1/RD2 Write signals are false in the “write” stages.

## Slide 41: How do we fix this?
We could add a new “temp” register
  But we’re trying not to add new registers
Can we fix this without adding any new registers?

## Slide 42: SINGLEcycle swap?
What is the MAIN difficulty of implementing a “Swap” instruction in the SINGLEcycle Larc microarchitecture?

## Slide 43
PC
IM
address
instruction
RF
DM
RR1
RR2
WR
WD
RD1
RD2
address
RD
WD
0
1
2
3
SIGN EXTEND
<< 8
LIMM
ADD
0..0
[4..11]
0
1
ADD
00..01
SIGN EXTEND
SIGN EXTEND
ALU
z
RC[0..3]
RA[8..11]
LIMM
[0..7]
SIMM[8..11]
SIMM[0..3]
0
1
0
1
0
1
RFWRITE
RFWD
SE
LW
ALU
SUB
NOR
SW
RD1
2
RB[4..7]
BN
BE
0
1
0
1
JAL
SINGLEcycle Larc implementation

## Slide 44: On your own
On your own: think up an instruction to implement in MULTIcycle Larc
Be reasonable about modifications
  I.e., make only “gentle” modifications
Implement it in the datapath
Modify the CU
Analyze whether it’s feasible to implement your instruction in SINGLEcycle Larc