## Slide 1: Comp Sci 310
Day 26

## Slide 2: Announcements
Quiz 11 on Monday, 11/3
  Booth multiplication
    Similar to Quiz 9
Exam 2 on Friday, 11/7
  Should we do a review on Wednesday, 11/5?
    Otherwise, we start talking about optimizations to the control unit (not on exam 2)

## Slide 3: Another look at multiplication
The basic multiplication algorithm has limitations
  It’s inefficient!
  It doesn’t work with negative numbers
We will focus on efficiency first

## Slide 4: SINGLEcycle multiplication
Should we implement the basic multiplication algorithm in a SINGLEcycle datapath?
NO!
  Why not?
The clock cycle time would have to be large enough to accommodate the multiplication of two N-bit words.
What about a MULTIcycle implementation?

## Slide 5: Basic algorithm: efficiency
How do we quantify the (in)efficiency of the basic multiplication algorithm?
Assume a register size of N = 2k
How many shifts are needed?
2*N
How many additions are needed?
# of 1’s in the multiplier

## Slide 6: Room for improvement
Shifts are easier to do than additions
Let’s see if we can reduce the number of addition operations performed

## Slide 7: What if?
What if the multiplier (Q) contains long runs of 1’s?
M *00011111
--------
M = M*20
M0 = M*21
M00 = M*22
M000 = M*23
M0000 = M*24
-----------------------------------------
M*(00011111) = M*(24+23+22+21+20) = M*31
= M*(25-20) = M*(32-1)

## Slide 8: In general
The previous approach can be generalized to any run of 1’s of length p + 1
If Q =
Then
Q = 2k + 2k-1 + . . . + 2k-p + . . .
= . . . + (2k+1 – 2k-p) + . . .
. . . | 2k+1 | 2k | 2k-1 | 2k-2 | . . . | 2k-p | 2k-p-1 | . . .
. . . | 0 | 1 | 1 | 1 | . . . | 1 | 0 | . . .

## Slide 9: Some examples
0000 0011 1111 1100 = 29+28+27+26+25+24+23+22
= 210-22
= 1024-4
= 1020
0011 1100 0111 1010 = (213+212+211+210)+
(26+25+24+23)+21
= (214-210)+(27-23)+(22-21)
= 15482

## Slide 10: Booth’s multiplication algorithm
Start
A  0, Q-1  0,
M  Mcand, Q  Mplier, Count  N

## Slide 11: Booth’s multiplication algorithm
Q0, Q-1
Start
A  0, Q-1  0,
M  Mcand, Q  Mplier, Count  N

## Slide 12: Booth’s multiplication algorithm
Q0, Q-1
Start
Count  Count – 1
Arithmetic right shift: A, Q, Q-1
A  0, Q-1  0,
M  Mcand, Q  Mplier, Count  N
= 11 or 00

## Slide 13: Booth’s multiplication algorithm
Q0, Q-1
Start
A  A - M
Count  Count – 1
Arithmetic right shift: A, Q, Q-1
= 10
A  0, Q-1  0,
M  Mcand, Q  Mplier, Count  N
= 11 or 00

## Slide 14: Booth’s multiplication algorithm
Q0, Q-1
Start
A  A - M
A  A + M
Count  Count – 1
Arithmetic right shift: A, Q, Q-1
Count = 0?
= 10
= 01
A  0, Q-1  0,
M  Mcand, Q  Mplier, Count  N
= 11 or 00

## Slide 15: Booth’s multiplication algorithm
Q0, Q-1
Start
A  A - M
A  A + M
Count  Count – 1
Arithmetic right shift: A, Q, Q-1
Count = 0?
Done
= 10
No: < N repetitions
Yes: N repetitions
= 01
A  0, Q-1  0,
M  Mcand, Q  Mplier, Count  N
= 11 or 00