## Slide 1: Comp Sci 310
Day 32

## Slide 2: Announcements
Assignment 4 due on Monday, 11/17
  Assignment 5 posted by Wednesday, 11/19
    Assignment 5 due Wednesday, 12/3
Quiz 12: Monday, 11/17
  Advanced control unit

## Slide 3: The microcoded approach
Each control word is really a microinstruction
The control ROM stores a microprogram
  Microprogram memory (MM)
The state register is a microprogram counter (MPC)
The address select logic is a micro-control unit
So, the microprogramed CU is really a “micro-computer” inside the CPU

## Slide 4: Final analysis
Larc CU
Control ROM
S
T
A
T
E
4
opcode
control word
2
5
24
Dispatch ROM
1
0
3
One ROM = 14848 bits
Two ROMs = 29*5 + 25*29 = 2560 + 928 = 3488 bits
Dispatch ROM + Control ROM = …
… 24*5 + 25*26 = … 80+ 832 = 912 bits

## Slide 5: Perspectives on microcoded control
Microcoding reduces the CPU design task to a more manageable programming problem
Specialized programmers build the table of control signals that make up the ROM symbolically
Then they use a microassembler to convert this symbolic program into actual ROMs after debugging with simulators
  A.k.a., firmware

## Slide 6: Hardwiring vs. microcoding (1)
Both approaches start with the same functional description of the CPU
  They use different schemes to generate the control signals
CPUs with hardwired control are faster than microcoded CPUs because…
  ROMs are slower than logic gate delays
CPUs with microcoded control are faster, easier and cheaper TO DESIGN

## Slide 7: Hardwiring vs. microcoding (2)
Use hardwired control for ISAs that are simple and/or CPUs that require fast execution
Microcoded control is used in complex designs and to keep manufacturing costs relatively low

## Slide 8: So long, MULTIcycle!!
PC
M
IR
MDR
RF
RD1
RD2
ALUOUT
SIGN EXTEND
SHL8
SIGN EXTEND
SIGN EXTEND
1
0
z
ALU
CONTROL UNIT
M Write
PC Write
M Src
IR write
MDR write
LI
LW
SorL
RD1 Write
RD2 Write
ALU2
ALU1
SUB
NOR
ALUout Write
BE
BN
BN
BE
JAL
RFWD
2
OPCODE[12..15]
LIMM[4..11]
SIMM[0..3]
SIMM[8..11]
LIMM
[0..7]
RA[8..11]
RC[0..3]
RB[4..7]
10
01
00
11
2
2
RF Write

## Slide 9: Welcome back, SINGLEcycle!
PC
IM
address
instruction
RF
DM
RR1
RR2
WR
WD
RD1
RD2
address
RD
WD
0
1
2
3
SIGN EXTEND
<< 8
LIMM
ADD
0..0
[4..11]
0
1
ADD
00..01
SIGN EXTEND
SIGN EXTEND
ALU
z
RC[0..3]
RA[8..11]
LIMM
[0..7]
SIMM[8..11]
SIMM[0..3]
0
1
0
1
0
1
RFWRITE
RFWD
LW
SUB
NOR
SW
RD1
2
RB[4..7]
BN
BE
0
1
0
1
JAL
CONTROL UNIT
OPCODE[12..15]
SE
ALU
MEMWRITE

## Slide 10: CPU Performance for different micro-architectures
SINGLEcycle micro-architecture
  CPI?
  CCT?
MULTIcycle micro-architecture
  CPI?
  CCT?

## Slide 11: Stylized representation of SINGLEcycle
Each phase in the instruction cycle is named after the physical functional unit that is active during that stage
Note that there are two distinct memory units (Harvard architecture)
  One for instructions (IM)
  One for data (DM)
What is the meaning of the shading?
When a unit is half-shaded:
  If its right half is shaded, then it means…
  If its right half is shaded, then it means…
What is the above instruction?
I M
R F
D M
R F
ALU

## Slide 12: How fast can we do laundry?

## Slide 13: Laundry times
Cleaning cycle: washing  drying  folding  put-away
Cleaning cycle time (CCT) = 2 hours
  During these two hours, washing, drying, folding and putting clothes away must all be completed!

## Slide 14: SINGLEcycle laundry
Load 1
Two loads of laundry = 4 hours of work
Each load must be completed before moving onto the next one…
Load 2

## Slide 15: New laundry times
Cleaning cycle time (CCT) = 2 hours
  During these two hours, washing, drying, folding and putting clothes away must all be completed!
Each one of the sub-tasks takes 30 minutes

## Slide 16: MULTIcycle laundry
Step 1
Two loads of laundry = ???
Each step must be completed before moving onto the next one…
Step 2
Step 4
Step
3
Step 5
Step 6
Step
7
Step 8

## Slide 17: MULTIcycle laundry
Step 1
Two loads of laundry = 4 hours of work
Each step must be completed before moving onto the next one…
Step 2
Step
3
Step 4
Step 5
Step 6
Step
7
Step 8

## Slide 18: Pipelining
The previous two approaches are non-pipelined ways of doing laundry
Pipelined approach: as soon as the washer is finished with the first load and placed in the dryer, load the washer with the second dirty load...

## Slide 19: Pipelining: laundry analogy
Step 1
Step 2
Step
3
Step 4
Step 5
Step 6
Step
7
Step 8

## Slide 20: Pipelining: laundry analogy
Step 1
Step 2
Step
3
Step 4
Step 5
Step 6

## Slide 21: Pipelining: laundry analogy
Step 1
Step 2
Step
3
Step 4
Step 5
Step 6
TWO loads of laundry = 2.5 hours of work!!
Speed up: 4 / 2.5 = 1.6
How many loads of laundry can we do in 2 hours?

## Slide 22: Pipelining
Pipelining is an implementation technique in which multiple instructions are overlapped in execution
Today, pipelining is nearly universal

## Slide 23: Pipelined instruction execution (1)
To apply the pipelining approach to instruction execution by a CPU, we assume that the instruction cycle can be split into several stages
  Each takes the same amount of time
  Think MULTIcycle
The CPU moves each instruction through each consecutive stage in the pipeline
Each stage takes ONE clock cycle
  Just like MULTIcycle

## Slide 24: Pipelined instruction execution (2)
The number of stages in the pipeline is called the length of the pipeline
A new instruction is issued (starts executing) every cycle, but it will not complete until several cycles later
  How many?
Several instructions are executing in parallel but there is only one instruction in each stage at any given time

## Slide 25: Pipelining: latency
How much faster is each individual instruction executed compared to the SINGLEcycle approach?
In other words: by how much is each instruction’s latency decreased?
  Latency = time it takes for an instruction to execute.

## Slide 26: Pipeline performance
We’re going to compare the performance of a pipeline micro-architecture to that of a SINGLEcycle micro-architecture
Stages:
  IF
  ID
  EX
  MEM
  WB
  Go back to 1 for next instruction

## Slide 27: Pipeline performance formula
Will performance go up or down?
Time between instructions (pipelined) =
Time between instructions (non-pipelined)
---------------------------------------------------------
Number of pipe stages

## Slide 28: Example (1)
Assume the following operation times for the major functional units:
 | Memory unit | ALU and adders | Register file | Muxes, CU, etc.
Operation time | 200ps | 200ps | 100ps | negligible
Instruction class
Instruction fetch
Register read
ALU op
Data access
Register write
Total time
Load
200ps
100ps
200ps
200ps
100ps
800ps
Store
200ps
100ps
200ps
200ps
700ps
ALU
200ps
100ps
200ps
100ps
600ps
Branches
200ps
100ps
200ps
500ps

## Slide 29: Example (2)
CC# | 1 |  |  |  |  | 2 |  |  |  |  | 3 |  |  |  | 
 | IF | ID | EX | MEM | WB | IF | ID | EX | MEM | WB | IF | ID | EX | MEM | WB
 | 800 |  |  |  |  | 800 |  |  |  |  | 800 |  |  |  | 
SINGLEcycle: clock cycle large enough to handle all five stages (800ps)
Time from start of first to start of fourth instruction = …
…3*800 = 2400ps
What about pipelining?
CC# | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  |  | 
B |  | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  | 
C |  |  | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  | 
 | 0 | 200 | 400 | 600 | 800 | 1000 | 1200 | 1400 |  |  |  |  |  |  | 
A = lw R0 0(R1)
B = lw R2 1(R3)
C = lw R4 2(R5)
Time from start of first to start of fourth instruction = …
…3*200 = 600ps
Fourfold improvement in performance!

## Slide 30: But wait!
Time between instructions (pipelined) =
Time between instructions (non-pipelined)
---------------------------------------------------------
Number of pipe stages
This formula suggests a fivefold speedup, but in our example, we saw only a fourfold speedup.

## Slide 31: Total execution time
The fourfold improvement is not even seen in total execution time
  SINGLEcycle: 2400ps
  Pipelined: 1400ps
  2400 / 1400 < 4
Why?
Because the example was too small…