## Slide 1: Comp Sci 310
Day 33

## Slide 2: Announcements
Assignment 4 due tonight at 11:59 PM
  Assignment 5 posted by Wednesday, 11/19
    Assignment 5 due Wednesday, 12/3
      Assessment component (online form)
Quiz 13: Friday, 11/21
  Pipeline micro-architecture
Quiz 14(last quiz): 12/3 or 12/5
  Memory
Wrap-up / review: 12/8
Exam 3(part 1): 12/10
  Old stuff
Exam 3(part 2): 12/12
  New stuff

## Slide 3: Pipeline performance formula
Using pipelining, will performance go up or down?
Time between instructions (pipelined) =
Time between instructions (non-pipelined)
---------------------------------------------------------
Number of pipe stages

## Slide 4: Example (1)
Assume the following operation times for the major functional units:
 | Memory unit | ALU and adders | Register file | Muxes, CU, etc.
Operation time | 200ps | 200ps | 100ps | negligible
Instruction class
Instruction fetch
Register read
ALU op
Data access
Register write
Total time
Load
200ps
100ps
200ps
200ps
100ps
800ps
Store
200ps
100ps
200ps
200ps
700ps
ALU
200ps
100ps
200ps
100ps
600ps
Branches
200ps
100ps
200ps
500ps

## Slide 5: Example (2)
CC# | 1 |  |  |  |  | 2 |  |  |  |  | 3 |  |  |  | 
 | IF | ID | EX | MEM | WB | IF | ID | EX | MEM | WB | IF | ID | EX | MEM | WB
 | 800 |  |  |  |  | 800 |  |  |  |  | 800 |  |  |  | 
SINGLEcycle: clock cycle large enough to handle all five stages (800ps)
Time from start of first to start of fourth instruction = …
…3*800 = 2400ps
What about pipelining?
CC# | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  |  | 
B |  | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  | 
C |  |  | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  | 
 | 0 | 200 | 400 | 600 | 800 | 1000 | 1200 | 1400 |  |  |  |  |  |  | 
A = lw R0 0(R1)
B = lw R2 1(R3)
C = lw R4 2(R5)
Time from start of first to start of fourth instruction = …
…3*200 = 600ps
Fourfold improvement in performance!

## Slide 6: But wait!
Time between instructions (pipelined) =
Time between instructions (non-pipelined)
---------------------------------------------------------
Number of pipe stages
This formula suggests a fivefold speedup, but in our example, we saw only a fourfold speedup.

## Slide 7: Total execution time
The fourfold improvement is not even seen in total execution time
  SINGLEcycle: 2400ps
  Pipelined: 1400ps
  2400 / 1400 < 4
Why?
Because the example was too small…

## Slide 8: More instructions
What if we increase the number of instructions executed?
What is the improvement factor?

## Slide 9: Add 1000000 more instructions
CC# | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | … | ??? | ??? | ??? | ??? | ??? | 
1 | IF | ID | EX | MEM | WB |  |  |  |  |  |  | … |  |  |  |  |  | 
2 |  | IF | ID | EX | MEM | WB |  |  |  |  |  | … |  |  |  |  |  | 
3 |  |  | IF | ID | EX | MEM | WB |  |  |  |  | … |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
106+3 |  |  |  |  |  |  |  |  |  |  |  | . |  |  |  |  |  | 
 | 0 | 200 | 400 | 600 | 800 | 1000 | 1200 | 1400 |  |  |  | … |  |  |  |  |  | X
X = ???
106*200 + 1400 = 200001400ps
CC# | 1 |  |  |  |  | 2 |  |  |  |  | 3 |  |  |  |  | 4 | … | ??? | 
 | IF | ID | EX | MEM | WB | IF | ID | EX | MEM | WB | IF | ID | EX | MEM | WB |  | … |  | 
 | 0 |  |  |  |  | 800 |  |  |  |  | 1600 |  |  |  |  | 2400 | … |  | Y
Y = ???
106*800 + 2400= 800002400ps
800002400 / 200001400 ≈ 4.0

## Slide 10: Perfectly balanced
In a big example, we saw the fourfold improvement
Why not a fivefold improvement?
The stages aren’t perfectly balanced!
  SINGLEcycle: 800ps
  Pipeline stage: 200ps
What ratio does the fourfold increase represent?
CC# | 1 | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A | IF |  | ID | EX |  | MEM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  | 
B |  | IF |  |  | ID | EX |  | MEM |  | WB |  |  |  |  |  |  |  |  |  |  | 
C |  |  |  | IF |  |  | ID | EX |  | MEM |  | WB |  |  |  |  |  |  |  |  | 
 | 0 | 200 |  | 400 |  | 600 |  | 800 |  | 1000 |  | 1200 |  | 1400 |  |  |  |  |  |  | 

## Slide 11: Real total execution times
Total execution times for programs on nonpipelined to pipelined processors is closer to the ratio of times between instructions
Balanced pipeline stages implies ...
  ... total execution times on nonpipelined to pipelined processors is the _____??______
    length of the pipe

## Slide 12: Performance summary
Pipelining improves performance by increasing throughput
Does not decrease execution time of an individual instruction
Instruction throughput is THE important metric, because… ???
  … real programs execute billions of instructions!

## Slide 13: Sample code
Same machine language program fragment…
…Executed on one of the Larc implementations:
SINGLE
  CPI?
  CCT?
MULTI
  CPI?
  CCT?
PIPELINE
  CPI?
  CCT?
li R1 9
li R2 10
li R3 3
li R4 4
li R5 5
lw R3 0(R1)
add R3 R1 R2
sw 0(R2) R2

## Slide 14: Sample code
Same machine language program fragment…
…Executed on one of the Larc implementations:
SINGLE
  CPI? 1.0
  CCT? MEM+RF+ALU+MEM+RF
MULTI
  CPI?
  CCT?
PIPELINE
  CPI?
  CCT?
li R1 9
li R2 10
li R3 3
li R4 4
li R5 5
lw R3 0(R1)
add R3 R1 R2
sw 0(R2) R2

## Slide 15: Sample code
Same machine language program fragment…
…Executed on one of the Larc implementations:
SINGLE
  CPI? 1.0
  CCT? MEM+RF+ALU+MEM+RF
MULTI
  CPI?
  CCT?
PIPELINE
  CPI?
  CCT?
li R1 9
li R2 10
li R3 3
li R4 4
li R5 5
lw R3 0(R1)
add R3 R1 R2
sw 0(R2) R2
Two cycles for each LI (IF, ID)
Five cycles for LW
Four cycles for ADD
Four cycles for SW
---------------------------------------
Total cycles = 2*5 + 2*4 + 5 = 23

## Slide 16: Sample code
Same machine language program fragment…
…Executed on one of the Larc implementations:
SINGLE
  CPI? 1.0
  CCT? MEM+RF+ALU+MEM+RF
MULTI
  CPI? 23/8
  CCT? MAX{MEM, RF, ALU}
PIPELINE
  CPI?
  CCT?
li R1 9
li R2 10
li R3 3
li R4 4
li R5 5
lw R3 0(R1)
add R3 R1 R2
sw 0(R2) R2
Two cycles for each LI (IF, ID)
Five cycles for LW
Four cycles for ADD
Four cycles for SW
---------------------------------------
Total cycles = 2*5 + 2*4 + 5 = 23

## Slide 17: Sample code
Same machine language program fragment…
…Executed on one of the Larc implementations:
SINGLE
  CPI? 1.0
  CCT? MEM+RF+ALU+MEM+RF
MULTI
  CPI? 23/8
  CCT? MAX{MEM, RF, ALU}
PIPELINE
  CPI?
  CCT?
li R1 9
li R2 10
li R3 3
li R4 4
li R5 5
lw R3 0(R1)
add R3 R1 R2
sw 0(R2) R2
9 cycles for LI
1 more for LW
1 more for ADD
1 more for SW
---------------------------------------
Total cycles = 9+3=12

## Slide 18: Sample code
Same machine language program fragment…
…Executed on one of the Larc implementations:
SINGLE
  CPI? 1.0
  CCT? MEM+RF+ALU+MEM+RF
MULTI
  CPI? 23/8
  CCT? MAX{MEM, RF, ALU}
PIPELINE
  CPI? 12/8
  CCT? MAX{MEM, RF, ALU}
li R1 9
li R2 10
li R3 3
li R4 4
li R5 5
lw R3 0(R1)
add R3 R1 R2
sw 0(R2) R2
9 cycles for LI
1 more for LW
1 more for ADD
1 more for SW
---------------------------------------
Total cycles = 9+3=12