## Slide 1: Comp Sci 310
Day 35

## Slide 2: Announcements
Assignment 5 due Wednesday, 12/3
  Partner(s) / self assessment component (online form)
Quiz 14(last quiz): 12/3 or 12/5
Wrap-up / review: 12/8
Exam 3(part 1): 12/10
  Old stuff
Exam 3(part 2): 12/12
  New stuff

## Slide 3: Pipeline hazards
There are situations in pipelining when the next instruction cannot execute in the following clock cycle
These events are called hazards
Three different types:
  Structural
  Data
  Control

## Slide 4: Data hazards
Data hazards occur when the pipeline must be stalled (with a “no op”) because one step must wait for another to complete
Laundry: unmatched sock?
  Run to your room and search for the match
    In the meantime, the laundry pipeline is stalled.

## Slide 5: Example data hazard
Data hazards arise from the dependence of one instruction on an earlier one that is still in the pipeline
Example: ADD R0 R1 R2 SUB R3 R0 R4
Why is this bad?
The ADD doesn’t write its result until the fifth (final) stage
  The SUB has to wait for ADD to write its result before it can read from the register file

## Slide 6: Handling data hazards
How should the pipeline handle this? ADD R0 R1 R2 SUB R3 R0 R4
Rely on compilers to remove all such hazards?
No!
Solution: forwarding

## Slide 7: Forwarding
Assume: ADD R0 R1 R2 SUB R3 R0 R4
Do we need to wait for R1+R2 to be written to R0? (this is called a pipeline “stall”, accomplished via a “no-op”)
  No!
Compute it, and then feed it directly to the ALU phase in the execution of the SUB instruction
This is the essence of forwarding

## Slide 8: Forwarding example
IM
R F
DM
R F
ALU
IM
R F
DM
R F
ALU
ADD R0 R1 R2
SUB R3 R0 R4

## Slide 9: Forwarding to avoid every stall?
Can forwarding be used to prevent all pipeline stalls?
No!
Example?

## Slide 10: Another example
IM
R F
DM
R F
ALU
IM
R F
DM
R F
ALU
LW R0 0(R1)
ADD R3 R0 R4
Now what happens?

## Slide 11: You can’t do that!
IM
R F
DM
R F
ALU
IM
R F
DM
R F
ALU
LW R0 0(R1)
ADD R3 R0 R4
Why not?

## Slide 12: You can’t do that!
IM
R F
DM
R F
ALU
IM
R F
DM
R F
ALU
LW R0 0(R1)
ADD R3 R0 R4
In this case, we must stall for one stage, and then we can … ???

## Slide 13: A valid forwarding path after stalling
IM
R F
DM
R F
ALU
LW R0 0(R1)
IM
R F
DM
R F
ALU
ADD R3 R0 R4
This scenario is called a load-use data hazard

## Slide 14: Over-simplification
IM
R F
DM
R F
ALU
LW R0 0(R1)
IM
R F
DM
R F
ALU
ADD R3 R0 R4
Note that this is really just a simplification, because…
…among other things, we are stalling before we even know it’s an ADD

## Slide 15: Reordering code to avoid stalls
a = b + e;
c = b + f;
Find the hazards!
Draw a diagram!
lw r1 0(r0)
lw r2 1(r0)
add r3 r1 r2
sw 3(r0) r3
lw r4 2(r0)
add r5 r1 r4
sw 4(r0) r5

## Slide 16: With pictures
 | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 10 |  | 11 | 
lw | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  | 
lw |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  | 
sw |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB | 
lw r1 0(r0)
lw r2 1(r0)
add r3 r1 r2
sw 3(r0) r3
lw r4 2(r0)
add r5 r1 r4
sw 4(r0) r5

## Slide 17: Hazard #1
 | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 10 |  | 11 | 
lw | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  | 
lw |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  | 
sw |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB | 
lw r1 0(r0)
lw r2 1(r0)
add r3 r1 r2
sw 3(r0) r3
lw r4 2(r0)
add r5 r1 r4
sw 4(r0) r5

## Slide 18: Hazard #2
 | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 10 |  | 11 | 
lw | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  | 
lw |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  | 
sw |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB | 
lw r1 0(r0)
lw r2 1(r0)
add r3 r1 r2
sw 3(r0) r3
lw r4 2(r0)
add r5 r1 r4
sw 4(r0) r5

## Slide 19: Hazard #3
 | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 10 |  | 11 | 
lw | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  | 
lw |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  | 
sw |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB | 
lw r1 0(r0)
lw r2 1(r0)
add r3 r1 r2
sw 3(r0) r3
lw r4 2(r0)
add r5 r1 r4
sw 4(r0) r5

## Slide 20: Hazard #4
 | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 10 |  | 11 | 
lw | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  | 
lw |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  | 
sw |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB | 
lw r1 0(r0)
lw r2 1(r0)
add r3 r1 r2
sw 3(r0) r3
lw r4 2(r0)
add r5 r1 r4
sw 4(r0) r5

## Slide 21: Use forwarding
 | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 10 |  | 11 | 
lw | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  | 
lw |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  | 
sw |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB | 
lw r1 0(r0)
lw r2 1(r0)
add r3 r1 r2
sw 3(r0) r3
lw r4 2(r0)
add r5 r1 r4
sw 4(r0) r5
All of the data hazards can be resolved using forwarding…
… except the load-use hazards.

## Slide 22: Stall
 | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 10 |  | 11 | 
lw | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  | 
lw |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  | 
sw |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB | 
lw r1 0(r0)
lw r2 1(r0)
add r3 r1 r2
sw 3(r0) r3
lw r4 2(r0)
add r5 r1 r4
sw 4(r0) r5
We need to stall for this hazard.

## Slide 23: Stall
 | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 10 |  | 11 |  | 12 | 
lw | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | NO OP |  |  |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  | 
sw |  |  |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB | 
lw r1 0(r0)
lw r2 1(r0)
add r3 r1 r2
sw 3(r0) r3
lw r4 2(r0)
add r5 r1 r4
sw 4(r0) r5

## Slide 24: And this one
 | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 10 |  | 11 |  | 12 | 
lw | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | NO OP |  |  |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  | 
sw |  |  |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB | 
lw r1 0(r0)
lw r2 1(r0)
add r3 r1 r2
sw 3(r0) r3
lw r4 2(r0)
add r5 r1 r4
sw 4(r0) r5

## Slide 25: Another stall
 | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 10 |  | 11 |  | 12 |  |  | 
lw | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | NO OP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | NO OP |  |  |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  | 
sw |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB | 
lw r1 0(r0)
lw r2 1(r0)
add r3 r1 r2
sw 3(r0) r3
lw r4 2(r0)
add r5 r1 r4
sw 4(r0) r5

## Slide 26: Can now use forwarding
 | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 10 |  | 11 |  | 12 |  |  | 
lw | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | NO OP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | NO OP |  |  |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB |  |  | 
sw |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | IF |  | ID |  | EX |  | DM |  | WB | 
lw r1 0(r0)
lw r2 1(r0)
add r3 r1 r2
sw 3(r0) r3
lw r4 2(r0)
add r5 r1 r4
sw 4(r0) r5

## Slide 27: Reordering code to avoid stalls
a = b + e;
c = b + f;
Reorder the code to avoid stalls!
lw r1 0(r0)
lw r2 1(r0)
add r3 r1 r2
sw 3(r0) r3
lw r4 2(r0)
add r5 r1 r4
sw 4(r0) r5

## Slide 28: REORDERED code to avoid stalls
a = b + e;
c = b + f;
Are there any hazards?
How much faster is this code than the previous code?
lw r1 0(r0)
lw r2 1(r0)
lw r4 2(r0)
add r3 r1 r2
sw 3(r0) r3
add r5 r1 r4
sw 4(r0) r5

## Slide 29: Examples
Sequence #1
LW R0 0(R0)
ADD R1 R0 R0
LI R0 17
SUB R2 R0 R0
Sequence #2
LI R0 1
LI R1 2
ADD R3 R0 R1
Sequence #3
LW R1 0(R4)
ADD R3 R1 R1
LI R2 1
Must the sequence stall?
Can the sequence avoid stalls, using only forwarding?
Can the sequence execute without stalling or forwarding?
What about reordering the code sequences that must stall?