## Slide 1: Comp Sci 310
Day 36

## Slide 2: Announcements
Assignment 5 due Wednesday, 12/3
  Partner(s) / self assessment component (online form)
Quiz 14(last quiz): 12/3
Wrap-up / review: 12/8
Exam 3(part 1): 12/10
  Old stuff
Exam 3(part 2): 12/12
  New stuff

## Slide 3: Pipeline hazards
There are situations in pipelining when the next instruction cannot execute in the following clock cycle
These events are called hazards
Three different types:
  Structural
  Data
  Control

## Slide 4: Thus far
We have seen hazards involving:
  Arithmetic operations
  Data transfers
What about branch instructions?

## Slide 5: Branch hazards
An instruction must be fetched at every clock cycle to sustain the pipeline
When is the branch decision made?
  After the EX stage (in the MEM stage)
The delay needed after a branch (in order to determine the outcome) is called a branch hazard

## Slide 6: Branch in the pipeline
I M
R F
D M
R F
ALU
10:beq r1 r2 21
11:and r12 r2 r5
12:or r13 r6 r2
13:add r14 r2 r2
21:lw r4 5(r7)
I M
R F
D M
R F
ALU
I M
R F
D M
R F
ALU
I M
R F
D M
R F
ALU
I M
R F
D M
R F
ALU

## Slide 7: Stalling
Stalling after a branch requires stalling three stages (IF, ID, EX)
Improvement: if we can move the branch execution to the ID stage, then fewer stalls are needed and instructions need to be flushed
This means the penalty for a branch taken (predicting wrong) is…
…only one instruction
Details omitted

## Slide 8: What NOT to do
What if we ALWAYS stall after a branch instruction?
Stalling gives us time to determine which instruction to fetch next

## Slide 9: Example
Assume all non-branch instructions have a CPI of 1
Best case: stall one instruction
In real programs: branches make up roughly 17% of the instructions
What is the (relative) slowdown?
  1.17 (BEST CASE)
Always stalling is just too SLOW!

## Slide 10: Handling branch hazards
Branch hazards:
  Are relatively simple to understand
  Occur less frequently than data hazards
Nothing as effective against branch hazards as forwarding is against data hazards
Therefore, simpler handling schemes are used
We will look at two basic prediction schemes

## Slide 11: Assume branch not taken
Just assume the branch is never taken
  Static branch prediction
Execution continues sequentially
What happens if the branch IS taken?
Then the instructions that were fetched and are now executing must be discarded / flushed

## Slide 12: Example
If branches are untaken 55% of the time, what is the relative speedup over always stalling?
  Assuming the “cost” to flush instructions is negligible
55% of the time, we don’t have to “pay” for a branch hazard stall
  E.g., 100 branches; slower = 100 stalls; faster = 45 stalls
Relative speedup: 100/45 = 2.222222…

## Slide 13: Dynamic branch prediction
Static branch prediction, along with compiler-based prediction is probably adequate for Larc
For deeper pipelines, what happens to the branch penalty, in terms of the number of instructions that need to be flushed?
  It increases
  It decreases
Dynamic branch prediction needed!
  Prediction of branches at runtime using runtime information

## Slide 14: One approach
Use a branch history table
  Small memory indexed by… ???
  … the low-order address bits of the branch instruction
The memory contains a bit that indicates whether the branch (to that address) was taken or not 1 – take the branch 0 – don’t take the branch
Not always CORRECT

## Slide 15: A shortcoming
The simple 1-bit prediction scheme has a performance shortcoming
Even if a branch is almost always taken, we can predict incorrectly twice
  Rather than just once!

## Slide 16: 1-bit prediction example
Consider a loop branch that branches nine times in a row, then is not taken once
What is the prediction accuracy for this branch, assuming the prediction bit for this branch remains in the prediction table

## Slide 17: 1-bit prediction solution
Wrong on the first and last iterations
Last: The branch was taken nine times in a row, so the bit is set but the branch is not taken after the last iteration
First: The branch was previously not taken, but now it must be taken in order to continue iterations of the loop
Branch is taken 90% of the time
What is the prediction accuracy?
80% 8 correct predictions, 2 incorrect

## Slide 18: Another approach
Instead of using 1 bit to tell whether the branch was taken or not, use 2 bits
The prediction must be wrong twice before it is changed
  Draw a finite state diagram for this scheme
Increment the prediction count every time you predict taken
Decrement every time you predict not taken
If the count is greater than 1, predict the branch is taken, otherwise predict it is not taken

## Slide 19: 2-bit prediction solution
Does the 2-bit prediction scheme help in the previous example?
Yes!
When the loop exits, after 9 iterations, the prediction count is 2 (decremented from 3)
2 is greater than 1, so the branch after the first iteration is correctly predicted to be taken

## Slide 20: Starting value
At what value should the branch instruction counts start?
What if the branch instruction count starts at 1?

## Slide 21: A general approach
The 2-bit prediction scheme can be generalized to n-bits
Increment the n-bit counter when the prediction is correct, decrement otherwise
Use the mid-point of the range as the division between taken and not taken
  I.e., if the counter value is greater than 2n-1 – 1

## Slide 22: Example
Consider three branch prediction schemes
  Predict not taken
  Predict taken
  Dynamic prediction
Assume they all have zero penalty when they predict correctly and two cycles when they are wrong.
Assume that the average predict accuracy of the dynamic predictor is 90%.
Which predictor is the best choice for the following branches?
  Branch taken with 5% frequency
  Branch taken with 95% frequency
  Branch taken with 70% frequency

## Slide 23: Solution
Branch taken with 5% frequency
  Predict not taken?
  Predict taken?
  Dynamic prediction?
Branch taken with 95% frequency
  Predict not taken?
  Predict taken?
  Dynamic prediction?
Branch taken with 70% frequency
  Predict not taken?
  Predict taken?
  Dynamic prediction?

## Slide 24: Solution
Branch taken with 5% frequency
  Predict not taken?
  Predict taken?
  Dynamic prediction?
Branch taken with 95% frequency
  Predict not taken?
  Predict taken?
  Dynamic prediction?
Branch taken with 70% frequency
  Predict not taken?
  Predict taken?
  Dynamic prediction?

## Slide 25: Solution
Branch taken with 5% frequency
  Predict not taken?
  Predict taken?
  Dynamic prediction?
Branch taken with 95% frequency
  Predict not taken?
  Predict taken?
  Dynamic prediction?
Branch taken with 70% frequency
  Predict not taken?
  Predict taken?
  Dynamic prediction?

## Slide 26: Solution
Branch taken with 5% frequency
  Predict not taken?
  Predict taken?
  Dynamic prediction?
Branch taken with 95% frequency
  Predict not taken?
  Predict taken?
  Dynamic prediction?
Branch taken with 70% frequency
  Predict not taken?
  Predict taken?
  Dynamic prediction?