## Slide 1: Comp Sci 310
Day 37

## Slide 2: Announcements
Assignment 5 due Wednesday, 12/3
  Partner(s) / self assessment component (online form)
Quiz 14(last quiz): 12/5
Wrap-up / review: 12/8
Exam 3(part 1): 12/10
  Old stuff
Exam 3(part 2): 12/12
  New stuff

## Slide 3: Why instruction sets became complex

## Slide 4: The semantic gap
Over the first few decades of the computer era, hardware has become cheaper
But software costs have increased tremendously!
Languages became more abstract to make programmers more productive
Therefore, the semantic gap between programming languages and hardware functionality has increased

## Slide 5: More complex instructions
As a result, more complex compilers were needed
Instead of bridging the gap with more powerful compilers, computer architects added more (complex) instructions to their ISA
Thus, compilers would be simpler to develop
Another benefit: executable programs would be smaller and therefore faster.
  How so?

## Slide 6: Disadvantages of complex instruction sets (1)
The more instructions means the more bits needed to represent the opcode
Since memory was still small and expensive, complex instructions with many parameters had to use complex encodings
  Complex instructions require more complex CUs
  Increase in instruction execution time in some cases

## Slide 7: Disadvantages of complex instruction sets (2)
Compilers tend to pick comparatively simpler instructions when generating code
  It is difficult to figure out whether a complex machine instruction is applicable to each specific situation
A large part of the “transistor budget” was devoted to implementing complex, but rarely used instructions
  Instead of improving the efficiency of the simpler, more heavily used instructions

## Slide 8: Reduced instruction set computer
RISC: Reduced Instruction Set Computers
  AIM: efficiency and pipelining
Each instruction does little work and takes little time to complete
In recent RISC machines, the number of instructions can be quite large

## Slide 9: RISC characteristics
Simpler, hardwired control units
Register-register ALU operations
Uniform, constant-length instruction format (a single word)
  Operands and opcodes in fixed locations
Large number of general-purpose registers
Pipelining is easier and efficient

## Slide 10: CPU design: conclusions
The design of the datapath and CU of a processor are guided by both the ISA and the available manufacturing technology
The ISA should be designed with implementation goals and constraints in mind
  Remember the RISC design principles
Pipelining is an example of ILP
Pipelining improves instruction throughput, not instruction execution latency
Pipelining techniques preserve the sequential programming model

## Slide 11: From CPU to memory
COMPUTER
MAIN MEMORY
I/O
SYSTEM
BUS
CPU
CPU
REGISTERS
Internal
BUS
Control
unit
ALU
Sequencing
logic
Control unit registers and decoders
Control
memory
Control
Unit

## Slide 12: From CPU to memory
COMPUTER
MAIN MEMORY
I/O
SYSTEM
BUS
CPU
We now turn our attention to memory

## Slide 13: Memory
The CPU has direct access to memory
NOT to external storage
Therefore, all instructions and data must be loaded into memory for the CPU to be able to fetch and process them
The ideal memory is:
  Accessed instantaneously by the CPU
  Free
  Infinitely large

## Slide 14
CPU
PROCESSOR REGISTER
CPU CACHE
L1 CACHE
L2 CACHE
L3 CACHE
PHYSICAL MEMORY
RANDOM ACCESS MEMORY
SOLID STATE MEMORY
NON-VOLATILE FLASH-BASED MEMORY
VIRTUAL MEMORY
FILE-BASED MEMORY
Processor
EDO, SD-RAM, DDR-SDRAM,
RD-RAM, etc.
SSD, Flash Drive
Mechanical
Hard Drive
$$$$$
$
Simplified computer memory hierarchy

## Slide 15: Principle of locality
The ideal memory does not exist
The memory hierarchy is used to create the illusion that there exists a large memory that can be accessed as fast as the fastest memory
This illusion is possible thanks to the principle of locality:
  Temporal locality, or locality in time
  Spatial locality, or locality in space

## Slide 16: Principle of locality and computer programs
The principle of locality underlies the way in which a typical program operates
If a variable is referenced, it will be referenced again soon (temporal locality)
If a variable is referenced, another variable defined near it will be referenced (spatial locality)

## Slide 17: An analogy
Cache / library desk
Main memory / library stacks

## Slide 18: Hit and miss
In many computer systems, the memory is a true hierarchy
That is, the contents of each level are “included” in the level below it
Let’s consider two adjacent levels of the hierarchy and define:
  The hit rate and the hit time
  The miss rate and the miss penalty
CPU
PROCESSOR REGISTER
CPU CACHE
L1 CACHE
L2 CACHE
L3 CACHE
PHYSICAL MEMORY
RANDOM ACCESS MEMORY
SOLID STATE MEMORY
NON-VOLATILE FLASH-BASED MEMORY
VIRTUAL MEMORY
FILE-BASED MEMORY
Processor
EDO, SD-RAM, DDR-SDRAM,
RD-RAM, etc.
SSD, Flash Drive
Mechanical
Hard Drive

## Slide 19: Hit
Hit rate (or hit ratio): the fraction of memory accesses found in the upper level
Hit time: time to access the upper level of memory
  Plus…
  …the time to determine if it’s a hit or miss

## Slide 20: Miss
Miss rate: the fraction of memory accesses NOT found in the upper level
  Equivalently: 1 – hit rate
Miss penalty: the time to replace a block in the upper level with a block from the lower level

## Slide 21: Cache and RAM organization: basic idea
CPU
Cache
Main memory
Word xfer
Block xfer
FAST
SLOW
CPU
L1
L2
L3
Main
Memory
FASTEST
FAST
LESS
FAST
SLOW

## Slide 22: Which are generally true?
Memory hierarchies take advantage of temporal locality
On a read, the value returned depends on which blocks are in the cache
Most of the cost of the memory hierarchy is at the highest level
Most of the capacity of the memory hierarchy is at the lowest level