## Slide 1: Comp Sci 310
Day 38

## Slide 2: Announcements
Assignment 5 due 12/8 at 11:59 PM
  Partner(s) / self assessment component (online form)
Quiz 14(last quiz): 12/5
Wrap-up / review: 12/8
Exam 3(part 1): 12/10
  Old stuff
Exam 3(part 2): 12/12
  New stuff

## Slide 3: Cache and RAM organization: basic idea
CPU
Cache
Main memory
Word xfer
Block xfer
FAST
SLOW
CPU
L1
L2
L3
Main
Memory
FASTEST
FAST
LESS
FAST
SLOW

## Slide 4: Which are generally true?
Memory hierarchies take advantage of temporal locality
On a read, the value returned depends on which blocks are in the cache
Most of the cost of the memory hierarchy is at the highest level
Most of the capacity of the memory hierarchy is at the lowest level

## Slide 5: Cache basics
Assume that the CPU requests one word at a time and that each cache block or cache line consists of a single word
Two questions arise:
  How do we know if the requested word is in the cache?
  If the requested word is in the cache, how do we find it?
The answers are related…

## Slide 6: Is a word in the cache?
If each word can go in exactly one place in the cache, then it is straightforward to find the word if it is in the cache
The simplest way to assign a location in the cache for each word in memory is to assign the cache location based on the address of the word in memory
Direct-mapped cache

## Slide 7: Direct-mapped cache
Each memory location is mapped directly to exactly one location in the cache:
000
001
010
011
100
101
110
111
00001
00101
01001
01101
10001
10101
11001
11101
<memory address of block> % <cache size in blocks>

## Slide 8: Direct-mapped cache
Each memory location is mapped directly to exactly one location in the cache:
000
001
010
011
100
101
110
111
<memory address of block> % <cache size in blocks>
00001
00101
01001
01101
10001
10101
11001
11101

## Slide 9: Direct-mapped cache
Each memory location is mapped directly to exactly one location in the cache:
000
001
010
011
100
101
110
111
<memory address of block> % <cache size in blocks>
00001
00101
01001
01101
10001
10101
11001
11101

## Slide 10: Direct-mapped cache
Given a memory address, how do you find the corresponding block in the cache?
000
001
010
011
100
101
110
111
<memory address of block> % <cache size in blocks>
00001
00101
01001
01101
10001
10101
11001
11101

## Slide 11: Is it the right one?
Each location in the cache can contain the contents of a number of different memory locations
How do we know whether the data in the cache corresponds to the requested word?
In other words, how do we know whether a requested word is in the cache or not?
Solution: we add a set of tags to the cache

## Slide 12: Tag information
The tag contains the address information required to identify whether a word in the cache corresponds to the requested word
What should it contain?
  The entire memory address?
    NO
  Only upper portion of the address
    the bits that are NOT used as an index into the cache
How do we know if the cache line is even valid?

## Slide 13: Valid information
We need a way to distinguish valid cache data from invalid cache data
When a processor starts up, the cache does not have good data and the tag fields will be meaningless
We need to know that the tag should be ignored for such entries
The most common solution: have a valid bit

## Slide 14: Caching: big picture
Caching is perhaps the most important example of the use of prediction
Using the principle of locality, cache systems try to predict data accesses
  When prediction is wrong, the system still returns the right value
In practice: the hit rates of cache on modern computers are often higher than 95%!

## Slide 15: Example
Consider a machine with an addressability of 32 words.
The cache, initially empty, contains 8 1-word blocks.
Show the contents of the cache after each one of the following memory references:
10110
11010
10110
11010
10000
00011
10000
10010
10000

## Slide 16
Index | V | Tag | Data
000 |  |  | 
001 |  |  | 
010 |  |  | 
011 |  |  | 
100 |  |  | 
101 |  |  | 
110 |  |  | 
111 |  |  | 

## Slide 17
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
 | 10110
 | 11010
 | 10110
 | 11010
 | 10000
 | 00011
 | 10000
 | 10010
 | 10000

## Slide 18
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
► | 10110
 | 11010
 | 10110
 | 11010
 | 10000
 | 00011
 | 10000
 | 10010
 | 10000

## Slide 19
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
 | 10110
► | 11010
 | 10110
 | 11010
 | 10000
 | 00011
 | 10000
 | 10010
 | 10000
HIT
MISS

## Slide 20
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | M[10110]
111 | N |  | 
 | 10110
► | 11010
 | 10110
 | 11010
 | 10000
 | 00011
 | 10000
 | 10010
 | 10000

## Slide 21
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | M[10110]
111 | N |  | 
 | 10110
 | 11010
► | 10110
 | 11010
 | 10000
 | 00011
 | 10000
 | 10010
 | 10000
HIT
MISS

## Slide 22
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | M[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | M[10110]
111 | N |  | 
 | 10110
 | 11010
► | 10110
 | 11010
 | 10000
 | 00011
 | 10000
 | 10010
 | 10000

## Slide 23
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | M[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | M[10110]
111 | N |  | 
 | 10110
 | 11010
 | 10110
► | 11010
 | 10000
 | 00011
 | 10000
 | 10010
 | 10000
HIT
MISS

## Slide 24
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | M[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | M[10110]
111 | N |  | 
 | 10110
 | 11010
 | 10110
 | 11010
► | 10000
 | 00011
 | 10000
 | 10010
 | 10000
HIT
MISS

## Slide 25
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | M[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | M[10110]
111 | N |  | 
 | 10110
 | 11010
 | 10110
 | 11010
 | 10000
► | 00011
 | 10000
 | 10010
 | 10000
HIT
MISS

## Slide 26
Index | V | Tag | Data
000 | Y | 10 | M[10000]
001 | N |  | 
010 | Y | 11 | M[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | M[10110]
111 | N |  | 
 | 10110
 | 11010
 | 10110
 | 11010
 | 10000
► | 00011
 | 10000
 | 10010
 | 10000

## Slide 27
Index | V | Tag | Data
000 | Y | 10 | M[10000]
001 | N |  | 
010 | Y | 11 | M[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | M[10110]
111 | N |  | 
 | 10110
 | 11010
 | 10110
 | 11010
 | 10000
 | 00011
► | 10000
 | 10010
 | 10000
HIT
MISS

## Slide 28
Index | V | Tag | Data
000 | Y | 10 | M[10000]
001 | N |  | 
010 | Y | 11 | M[11010]
011 | Y | 00 | M[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | M[10110]
111 | N |  | 
 | 10110
 | 11010
 | 10110
 | 11010
 | 10000
 | 00011
► | 10000
 | 10010
 | 10000

## Slide 29
Index | V | Tag | Data
000 | Y | 10 | M[10000]
001 | N |  | 
010 | Y | 11 | M[11010]
011 | Y | 00 | M[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | M[10110]
111 | N |  | 
 | 10110
 | 11010
 | 10110
 | 11010
 | 10000
 | 00011
 | 10000
► | 10010
 | 10000
HIT
MISS

## Slide 30
Index | V | Tag | Data
000 | Y | 10 | M[10000]
001 | N |  | 
010 | Y | 11 | M[11010]
011 | Y | 00 | M[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | M[10110]
111 | N |  | 
 | 10110
 | 11010
 | 10110
 | 11010
 | 10000
 | 00011
 | 10000
 | 10010
► | 10000
HIT
MISS

## Slide 31
Index | V | Tag | Data
000 | Y | 10 | M[10000]
001 | N |  | 
010 | Y | 10 | M[10010]
011 | Y | 00 | M[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | M[10110]
111 | N |  | 
 | 10110
 | 11010
 | 10110
 | 11010
 | 10000
 | 00011
 | 10000
 | 10010
► | 10000

## Slide 32
Index | V | Tag | Data
000 | Y | 10 | M[10000]
001 | N |  | 
010 | Y | 10 | M[10010]
011 | Y | 00 | M[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | M[10110]
111 | N |  | 
 | 10110
 | 11010
 | 10110
 | 11010
 | 10000
 | 00011
 | 10000
 | 10010
 | 10000
► | 
HIT
MISS

## Slide 33: Cache access
A referenced address must be divided into:
  A tag field (to identify the block in the cache line)
  A cache index (to select the cache line where the block is stored)
  A word or byte offset (when the amount of data requested by the CPU is smaller than the cache line)
The first two components uniquely identify the memory address of the block in each cache line

## Slide 34: Cache size
The size of the cache in blocks must be a power of 2, say 2n, where n is the…
… size of the cache index
The convention is for the size of the cache (e.g., 16KB) to refer to the data component only, not the bookkeeping info

## Slide 35: Example
How many total bits are required to build a direct-mapped cache with 16KB of data and 16 byte blocks, assuming a 32-bit address?
Memory is byte addressable.