## Slide 1: Comp Sci 310
Day 11

## Slide 2: Announcements
Quiz 5 on Monday, 9/29
Assignment 2 is due next Wednesday
  Submit solutions via d2l

## Slide 3: Other memory chips
We will need the following memory chips (build them in this order):
  RAM8
  RAM64
  RAM512
  RAM4K
  RAM16K
The only difference ?
  Answer: Their height (part of their name)
What are the only differences in their respective APIs?
  Answer: Address field gets bigger
What do you notice about the largest memory chip?
  Answer: It’s the largest memory that is a power-of-2-factor larger than the next largest memory
    What if we had RAM32K, but only 16 bit addresses?

## Slide 4: Recall: “RAM4” chip design
Mux4Way
R0
D
L
O
R1
D
L
O
R2
D
L
O
R3
D
L
O
DMux4Way
1
load
out
addr
in
How would you make RAM64?

## Slide 5: RAM64
Make a RAM64 chip out of 64 1-bit register chips.
??
Problems?
Need a Mux64Way!
What about a RAM16K?
Need a Mux16KWay!!

## Slide 6: RAM64
Make a RAM64 chip out of X RAM8 chips.

## Slide 7: RAM64
Make a RAM64 chip out of 8 RAM8 chips.

## Slide 8: Partial RAM64
Mux8Way
DMux8Way
1
load
out
addr
in
in
R8[0]
I
L
O
A
R8[1]
I
L
O
A
R8[2]
I
L
O
A
R8[3]
I
L
O
A
How to select the correct RAM8 chip?

## Slide 9: How to select the correct RAM8 chip?
RAM64 has height of 64
  Can store 64 words
Address needs to be ??? bits wide?
  Answer = 6, because 26 = 64
5
?
4
?
3
?
2
?
1
?
0
?
Bit position
Value of addr:
“which RAM8 chip”
“which address of the 23 words within the given RAM8 chip”
0 = LSB, 5 = MSB

## Slide 10: Partial RAM64
Mux8Way
DMux8Way
1
load
out
addr
in
in
R8[0]
I
L
O
A
R8[1]
I
L
O
A
R8[2]
I
L
O
A
R8[3]
I
L
O
A
How to select the correct RAM8 chip?

## Slide 11: RAM64
Mux8Way
DMux8Way
1
load
out
addr
in
in
R8[0]
I
L
O
A
R8[1]
I
L
O
A
R8[2]
I
L
O
A
R8[3]
I
L
O
A
Addr[3..5]
Addr[0..2]

## Slide 12: RAM64
Mux8Way
DMux8Way
1
load
out
addr
in
in
R8[0]
I
L
O
A
R8[1]
I
L
O
A
R8[2]
I
L
O
A
R8[3]
I
L
O
A
Addr[3..5]
Addr[0..2]
How would you make RAM512?

## Slide 13: Register file
RAM is outside the CPU
The CPU contains a small memory, called the register file
Our Larc computer will have a register file with the following properties:
  16 words in as many registers
  Words are 16 bits wide
  Two registers can be read out simultaneously
    Think about why this might be useful!
  One register can be loaded with a new value

## Slide 14: Dual-ported reading and writing
The two read ports continuously output the values in the two registers whose numbers are currently present at the two read inputs
  Combinational circuit
Don’t forget: the write operation only happens when the “load” input flag is set
  Sequential circuit (clocked)

## Slide 15: Register file (basic idea)
Register File

## Slide 16: Register file (basic idea)
Register File
Read register 1
Read register 2

## Slide 17: Register file (basic idea)
Register File
Read register 1
Read register 2
Write register

## Slide 18: Register file (basic idea)
Register File
Read register 1
Read register 2
Write register
Write data

## Slide 19: Register file (basic idea)
Register File
Read register 1
Read register 2
Write register
Write data
Write

## Slide 20: Register file (basic idea)
Register File
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Write

## Slide 21: API of the register file
/**
* Dual-ported register file of 16 registers, each 16 bits wide.
* The register file (RF) can be seen as a 1D array of length 16, with
* indices 0 through 15, in which each memory location contains a 16-bit value.
* The chip supports three simultaneous I/O operations, namely
* two read operations and one write operation, as follows:
* Read: rd1(t) = RF[rr1(t)](t)
* rd2(t) = RF[rr2(t)](t)
* Write: If load(t-1) == 1
* Then RF[wr(t-1)](t) = wd(t-1)
*/
CHIP RegisterFile {
IN rr1[????], // number of the first register to be read out
rr2[????], // number of the second register to be read out
wr[????], // number of the register to be written into
wd[????], // value to be written
load; // 1 if the value wd must be written to register number wr
OUT rd1[????], // current value in register number rr1
rd2[????]; // current value in register number rr2
PARTS:
// Implementation missing
}

## Slide 22: API of the register file
/**
* Dual-ported register file of 16 registers, each 16 bits wide.
* The register file (RF) can be seen as a 1D array of length 16, with
* indices 0 through 15, in which each memory location contains a 16-bit value.
* The chip supports three simultaneous I/O operations, namely
* two read operations and one write operation, as follows:
* Read: rd1(t) = RF[rr1(t)](t)
* rd2(t) = RF[rr2(t)](t)
* Write: If load(t-1) == 1
* Then RF[wr(t-1)](t) = wd(t-1)
*/
CHIP RegisterFile {
IN rr1[????], // number of the first register to be read out
rr2[????], // number of the second register to be read out
wr[????], // number of the register to be written into
wd[????], // value to be written
load; // 1 if the value wd must be written to register number wr
OUT rd1[????], // current value in register number rr1
rd2[????]; // current value in register number rr2
PARTS:
// Implementation missing
}

## Slide 23: API of the register file
/**
* Dual-ported register file of 16 registers, each 16 bits wide.
* The register file (RF) can be seen as a 1D array of length 16, with
* indices 0 through 15, in which each memory location contains a 16-bit value.
* The chip supports three simultaneous I/O operations, namely
* two read operations and one write operation, as follows:
* Read: rd1(t) = RF[rr1(t)](t)
* rd2(t) = RF[rr2(t)](t)
* Write: If load(t-1) == 1
* Then RF[wr(t-1)](t) = wd(t-1)
*/
CHIP RegisterFile {
IN rr1[ 4 ], // number of the first register to be read out
rr2[ 4 ], // number of the second register to be read out
wr[ 4 ], // number of the register to be written into
wd[ 16 ], // value to be written
load; // 1 if the value wd must be written to register number wr
OUT rd1[ 16 ], // current value in register number rr1
rd2[ 16 ]; // current value in register number rr2
PARTS:
// Implementation missing
}

## Slide 24: Register file schematic: read ports
Read register 1
Read register 2
Read data 1
Read data 2

## Slide 25: Register file schematic: read ports
Read register 1
Read register 2
Read data 1
Read data 2
R0
D
L
O
…
D
L
O
RN-2
D
L
O
RN-1
D
L
O

## Slide 26: Register file schematic: read ports
Read register 1
Read register 2
Read data 1
Read data 2
R0
D
L
O
MuxN
…
D
L
O
RN-2
D
L
O
RN-1
D
L
O
MuxN

## Slide 27: Register file schematic: read ports
Read register 1
Read register 2
Read data 1
Read data 2
R0
D
L
O
MuxN
…
D
L
O
RN-2
D
L
O
RN-1
D
L
O
MuxN

## Slide 28: Register file schematic: write port
How do you do this?

## Slide 29: Register file schematic: write port
R0
D
L
O
…
D
L
O
RN-2
D
L
O
RN-1
D
L
O
DMux
1
Write register
Write data
Write
???

## Slide 30: Example
Make a negative-edge triggered DFF.

## Slide 31: Positive-edge-triggered D flip-flop: implementation
D
Clock
Q
¬Q

## Slide 32: Negative-edge-triggered D flip-flop: implementation ???
D
Clock
Q
¬Q

## Slide 33: Negative-edge-triggered D flip-flop: implementation ???
D
Clock
Q
¬Q
Assume Q = 0,
Clock 1  0 and
D = 1

## Slide 34: Negative-edge-triggered D flip-flop: implementation ???
D
Clock
Q
¬Q
Assume Q = 0,
Clock 1  0 and
D = 1

## Slide 35: Negative-edge-triggered D flip-flop: implementation ???
D
Clock
Q
¬Q
Assume Q = 0,
Clock 1  0 and
D = 1

## Slide 36: Negative-edge-triggered D flip-flop: implementation ???
D
Clock
Q
¬Q
Assume Q = 0,
Clock 1  0 and
D = 1

## Slide 37: Negative-edge-triggered D flip-flop: implementation ???
D
Clock
Q
¬Q
Assume Q = 0,
Clock 1  0 and
D = 1

## Slide 38: Negative-edge-triggered D flip-flop: implementation ???
D
Clock
Q
¬Q
Assume Q = 0,
Clock 1  0 and
D = 1

## Slide 39: Negative-edge-triggered D flip-flop: implementation ???
D
Clock
Q
¬Q
Assume Q = 0,
Clock 1  0 and
D = 1

## Slide 40: Negative-edge-triggered D flip-flop: implementation ???
D
Clock
Q
¬Q
Assume Q = 0,
Clock 1  0 and
D = 1

## Slide 41: Negative-edge-triggered D flip-flop: implementation ???
D
Clock
Q
¬Q
Assume Q = 0,
Clock 1  0 and
D = 1

## Slide 42: Negative-edge-triggered D flip-flop: implementation ???
D
Clock
Q
¬Q
Assume Q = 0,
Clock 1  0 and
D = 1
Does this work in all cases?

## Slide 43: For fun!
Make a 3-bit “binary counter.”
The outputs should be the value of the counter
Use 3 DFFs and a “few” other gates (not too many more).
The counter should have one input: inc.
When the counter holds the value 7 (111), it should reset to 0 on increment.

## Slide 44: DFF counter
D
Q
C
D
Q
C
D
Q
C
INC
B2
B1
B0