## Slide 1: Comp Sci 310
Day 13

## Slide 2: Announcements
Assignment 2 is due on Monday, 10/6
  Submit solutions via d2l
Quiz 6 on Friday
  Register files, memory chips, and possibly whatever talk about today
One exam or two?
  You will definitely have an exam 11/7

## Slide 3: Here we are
COMPUTER
MAIN MEMORY
I/O
SYSTEM
BUS
CPU
CPU
REGISTERS
Internal
BUS
Control
unit
ALU

## Slide 4: Processing unit or CPU
The CPU’s role is data processor
  It performs arithmetic and other bit-level operations
Comprised of:
  The ALU (arithmetic logic unit) for integer operations
  Register file
  Control unit
  Interconnection among the previous components

## Slide 5: Machine instruction
The machine instruction is the fundamental unit of work. It specifies:
The opcode: the type of operation (add, subtract, etc.) to be performed
The operands: data (memory locations) to which the operation should be applied

## Slide 6: Instruction cycle
One complete instruction (a.k.a., fetch-execute) cycle can be split up:
Fetch: load the next instruction from memory
Decode: load values from registers and determine which action to take
Execute: carry out the operation on the operands (or compute the address for a “load” or “store” word instruction)
Memory access: read / write data from / to memory
Write back: write the result of the operation to the destination register
Another cycle starts as soon as the current cycle terminates (in an infinite loop)

## Slide 7: Processor implementation
We know about:
  The three factors that influence performance of computer systems: ???, ??? and ???
    What are they?
  The Larc ISA (see the Larc manual)
  The general structure of a computer
  Basic digital (combinational and sequential) circuits
Let’s build the first generation of Larc!

## Slide 8: CPU components
The datapath is comprised of all the units in the CPU that handle data processing:
  ALU (and other functional units, e.g., adders, floating-point units, etc.)
  Memory (e.g., cache), the register file and other registers
  Busses and other connections that move data around
The control unit tells the datapath elements (and RAM and I/O devices, which are outside the CPU) what to do and when

## Slide 9: A metaphor
The computer system as an orchestra
The datapath elements as the musicians
The control unit as the conductor

## Slide 10: A metaphor
The computer system as an orchestra
The datapath elements as the musicians
The control unit as the conductor

## Slide 11: First implementation
Our first generation Larc will have a single-cycle microarchitecture design
  Why?
Simplicity!
What is the CPI?

## Slide 12: Larc instruction set
Instruction type
Operation
Opcode
Semantics
addition
0000
Reg[RA] = Reg[RB] + Reg[RC]
subtraction
0001
Reg[RA] = Reg[RB] – Reg[RC]
multiplication
0010
To be implemented in the next generation
division
0011
NO HARDWARE IMPLEMENTATION
Logical left shift
0100
NO HARDWARE IMPLEMENTATION
Logical right shift
0101
NO HARDWARE IMPLEMENTATION
Bitwise NOR
0110
Reg[RA] = !(Reg[RB] | Reg[RC])
Set on less than
0111
If (Reg[RB]<Reg[RC]) Reg[BA]=1; else Reg[RA]=0
Load immediate
1000
Reg[RA] = sign_ext(LIMM)
Load upper immediate
1001
Reg[RA] = LIMM << 8
Branch equal to 0
1010
If (Reg[RC] == 0) PC = PC+sign_ext(LIMM)
Branch not equal to 0
1011
If (Reg[RC] != 0) PC = PC+sign_ext(LIMM)
Memory load
1100
Reg[RA] = Mem[Reg[RB] + sign_ext(SIMM)]
Memory store
1101
Mem[Reg[RB] + sign_ext(SIMM)] = Reg[RC]
Jump and link register
1110
Retn_addr=PC; PC=Reg[RB]; Reg[RA]=retn_addr;
Stop the computer
1111
???
ALU
Long immediate
Short immediate
Jump
HALT

## Slide 13: Encoding of Larc instructions
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
Opcode
Dest. Reg.
8-bit immediate
LIMM
Ra
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
Opcode
Dest. Reg.
Src. Reg. #1
Rb
Ra
Rc
Src. Reg. #2
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
Opcode
4-bit Imm. Value
Base Address
Rb
SIMM
Rc
Src. Reg.
li, lui
ALU ops
sw
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
Opcode
Dest. Reg.
Base Address
Rb
Ra
SIMM
4-bit Imm. Value.
lw
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
Opcode
8-bit Immediate Value
LIMM
Rc
Src. Reg.
beq, bne
jalr (or jal)
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
Opcode
Return Address
Target Address
Rb
Ra
Unused
halt
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
Opcode
Unused

## Slide 14: Larc instruction set
Instruction type
Operation
Opcode
Semantics
addition
0000
Reg[RA] = Reg[RB] + Reg[RC]
subtraction
0001
Reg[RA] = Reg[RB] – Reg[RC]
multiplication
0010
To be implemented in the next generation
division
0011
NO HARDWARE IMPLEMENTATION
Logical left shift
0100
NO HARDWARE IMPLEMENTATION
Logical right shift
0101
NO HARDWARE IMPLEMENTATION
Bitwise NOR
0110
Reg[RA] = !(Reg[RB] | Reg[RC])
Set on less than
0111
If (Reg[RB]<Reg[RC]) Reg[BA]=1; else Reg[RA]=0
Load immediate
1000
Reg[RA] = sign_ext(LIMM)
Load upper immediate
1001
Reg[RA] = LIMM << 8
Branch equal to 0
1010
If (Reg[RC] == 0) PC = PC+sign_ext(LIMM)
Branch not equal to 0
1011
If (Reg[RC] != 0) PC = PC+sign_ext(LIMM)
Memory load
1100
Reg[RA] = Mem[Reg[RB] + sign_ext(SIMM)]
Memory store
1101
Mem[Reg[RB] + sign_ext(SIMM)] = Reg[RC]
Jump and link register
1110
Retn_addr=PC; PC=Reg[RB]; Reg[RA]=retn_addr;
Stop the computer
1111
???
ALU
Long immediate
Short immediate
Jump
HALT
Why are “branch jumps” limited to 8 bits?

## Slide 15: Larc instruction set
Instruction type
Operation
Opcode
Semantics
addition
0000
Reg[RA] = Reg[RB] + Reg[RC]
subtraction
0001
Reg[RA] = Reg[RB] – Reg[RC]
multiplication
0010
To be implemented in the next generation
division
0011
NO HARDWARE IMPLEMENTATION
Logical left shift
0100
NO HARDWARE IMPLEMENTATION
Logical right shift
0101
NO HARDWARE IMPLEMENTATION
Bitwise NOR
0110
Reg[RA] = !(Reg[RB] | Reg[RC])
Set on less than
0111
If (Reg[RB]<Reg[RC]) Reg[BA]=1; else Reg[RA]=0
Load immediate
1000
Reg[RA] = sign_ext(LIMM)
Load upper immediate
1001
Reg[RA] = LIMM << 8
Branch equal to 0
1010
If (Reg[RC] == 0) PC = PC+sign_ext(LIMM)
Branch not equal to 0
1011
If (Reg[RC] != 0) PC = PC+sign_ext(LIMM)
Memory load
1100
Reg[RA] = Mem[Reg[RB] + sign_ext(SIMM)]
Memory store
1101
Mem[Reg[RB] + sign_ext(SIMM)] = Reg[RC]
Jump and link register
1110
Retn_addr=PC; PC=Reg[RB]; Reg[RA]=retn_addr;
Stop the computer
1111
???
ALU
Long immediate
Short immediate
Jump
HALT
What’s the point of adding an offset to a register value in memory load?

## Slide 16: Let’s build the datapath...

## Slide 17: Data path elements needed by all instructions
PC
IM
address
instruction
RF
RR1
RR2
WR
WD
RD1
RD2
All Larc instructions must be fetched from memory
All Larc instructions must access the register file

## Slide 18: Implementation of the fetch cycle
PC
IM
address
instruction
RF
RR1
RR2
WR
WD
RD1
RD2
RB[4..7]
ADD
00..01
RC[0..3]
RA[8..11]

## Slide 19: Implementation of the li?
PC
IM
address
instruction
RF
RR1
RR2
WR
WD
RD1
RD2
RB[4..7]
ADD
00..01
RC[0..3]
RA[8..11]
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
Opcode
Dest. Reg.
8-bit immediate
LIMM
Ra
Reg[RA] = sign_ext(LIMM)

## Slide 20: Implementation of the li
PC
IM
address
instruction
RF
RR1
RR2
WR
WD
RD1
RD2
RB[4..7]
ADD
00..01
SIGN EXTEND
RC[0..3]
RA[8..11]
LIMM
[0..7]
RFWRITE
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
Opcode
Dest. Reg.
8-bit immediate
LIMM
Ra
Reg[RA] = sign_ext(LIMM)