## Slide 1: Comp Sci 310
Day 2

## Slide 2: Bit significance
Bits are numbered 0, 1, 2, 3, … from right to left:
Least significant bit = bit in position 0
Most significant bit = bit on position 15 (or highest bit position)
How many numbers can be represented with 16 bits?
0000 0000 0000 0000(2) = 0(10) 0000 0000 0000 0001(2) = 1(10) 0000 0000 0000 0010(2) = 2(10) 0000 0000 0000 0011(2) = 3(10) . . . 1111 1111 1111 1101(2) = 65533(10) 1111 1111 1111 1110(2) = 65534(10) 1111 1111 1111 1111(2) = 65535(10)
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1

## Slide 3: Signed numbers
Previous examples showed unsigned numbers
  All bits used to represent the value of a number
Computer programs can calculate both positive and negative numbers
We need a way to distinguish positive from negative
Keep things simple: two’s complement
  Every computer today uses two’s complement binary representation for signed numbers

## Slide 4: Two’s complement
Leading 0’s mean positive
Leading 1’s mean negative
0000 0000 0000 0000(2) = 0(10) 0000 0000 0000 0001(2) = 1(10)
. . .
0111 1111 1111 1111(2) = 32767(10)
. . .
1000 0000 0000 0000(2) = -32768(10)
1000 0000 0000 0001(2) = -32767(10) . . . 1111 1111 1111 1110(2) = -2(10) 1111 1111 1111 1111(2) = -1(10)

## Slide 5: Question
What is the decimal value of this 16-bit two’s complement number? 1111 1111 1111 1100(2)
Answer = -4(10)

## Slide 6: Two useful operations
Two useful operations when working with two’s complement numbers
Negation
Sign extension

## Slide 7: Sign extension
Convert a binary number represented in n bits to a number represented with more than n bits
Shortcut: take the most significant bit from the smaller number – the sign bit – and replicate it to fill the new bits of the larger number

## Slide 8: Negation
Invert each bit (i.e., change 0 to 1, and 1 to 0)
Add one to the result
Based on observation that a number and its inverted representation must be 11…11: x + (¬x) = 11…11 = -1  x + (¬x) + 1 = 0

## Slide 9: Negation example
What is the 16-bit two’s complement representation of -1032(10)?
We know 1031(10) is 10000000111(2), so 1032(10) must be 10000001000(2).
With 16 bits (sign extension): 0000 0100 0000 1000(2)
Invert the bits: 1111 1011 1111 0111(2)
Add one: 1111 1011 1111 0111(2) 0000 0000 0000 0001(2) +
=
1111 1011 1111 1000(2)

## Slide 10: Question
What is the decimal value of this 16-bit two’s complement number?
1111 1111 1111 1000(2)
-8(10)

## Slide 11: Addition
A + B (A and B are both in two’s complement form)
Easy case: MSBs different
  Just add the numbers in binary
Same MSBs = have to check for overflow
Check the left two bits in the “carry” row

## Slide 12: Addition
1 0 1 1(2) -5(10) + 0 1 1 1(2) 7(10) --------- 2(10)

## Slide 13: Addition
1 0 1 1(2) -5(10) + 0 1 1 1(2) 7(10) --------- 0 2(10)

## Slide 14: Addition
1 1 0 1 1(2) -5(10) + 0 1 1 1(2) 7(10) --------- 0 2(10)

## Slide 15: Addition
1 1 0 1 1(2) -5(10) + 0 1 1 1(2) 7(10) --------- 1 0 2(10)

## Slide 16: Addition
1 1 1 0 1 1(2) -5(10) + 0 1 1 1(2) 7(10) --------- 1 0 2(10)

## Slide 17: Addition
1 1 1 0 1 1(2) -5(10) + 0 1 1 1(2) 7(10) --------- 0 1 0 2(10)

## Slide 18: Addition
1 1 1 1 0 1 1(2) -5(10) + 0 1 1 1(2) 7(10) --------- 0 1 0 2(10)

## Slide 19: Addition
1 1 1 1 0 1 1(2) -5(10) + 0 1 1 1(2) 7(10) --------- 0 0 1 0 2(10)

## Slide 20: Addition
1 1 1 1 1 0 1 1(2) -5(10) + 0 1 1 1(2) 7(10) --------- 0 0 1 0 2(10)

## Slide 21: Addition
1 1 1 1 1 0 1 1(2) -5(10) + 0 1 1 1(2) 7(10) --------- 0 0 1 0 2(10)

## Slide 22: Addition
1 1 1 1 NO OVERFLOW 1 0 1 1(2) -5(10) + 0 1 1 1(2) 7(10) --------- 0 0 1 0 2(10)

## Slide 23: Another addition example
0 1 1 0(2) 6(10) + 0 1 1 1(2) 7(10) --------- 13(10) INVALID!

## Slide 24: Another addition example
0 1 1 0(2) 6(10) + 0 1 1 1(2) 7(10) --------- 1 13(10) INVALID!

## Slide 25: Another addition example
0 0 1 1 0(2) 6(10) + 0 1 1 1(2) 7(10) --------- 1 13(10) INVALID!

## Slide 26: Another addition example
0 0 1 1 0(2) 6(10) + 0 1 1 1(2) 7(10) --------- 0 1 13(10) INVALID!

## Slide 27: Another addition example
1 0 0 1 1 0(2) 6(10) + 0 1 1 1(2) 7(10) --------- 0 1 13(10) INVALID!

## Slide 28: Another addition example
1 0 0 1 1 0(2) 6(10) + 0 1 1 1(2) 7(10) --------- 1 0 1 13(10) INVALID!

## Slide 29: Another addition example
1 1 0 0 1 1 0(2) 6(10) + 0 1 1 1(2) 7(10) --------- 1 0 1 13(10) INVALID!

## Slide 30: Another addition example
1 1 0 0 1 1 0(2) 6(10) + 0 1 1 1(2) 7(10) --------- 1 1 0 1 13(10) INVALID!

## Slide 31: Another addition example
0 1 1 0 0 1 1 0(2) 6(10) + 0 1 1 1(2) 7(10) --------- 1 1 0 1 13(10) INVALID!

## Slide 32: Another addition example
0 1 1 0 0 1 1 0(2) 6(10) + 0 1 1 1(2) 7(10) --------- 1 1 0 1 13(10) INVALID!

## Slide 33: Another addition example
0 1 1 0 OVERFLOW! 0 1 1 0(2) 6(10) + 0 1 1 1(2) 7(10) --------- 1 1 0 1 13(10) INVALID!

## Slide 34: Subtraction
Works basically the same way
Just check the left two bits in the “borrow” row for overflow
  What logical operation can you use to do this?

## Slide 35: Course overview
In CS251, you studied the architecture level, for some ISA
In this course: we focus mostly on microarchitecture, i.e., how the instruction set is implemented in hardware
We will study the principles of computer organization, i.e., how digital logic circuits are combined to execute machine instructions. We will focus mainly on the CPU and memory hierarchy.
We will apply these principles as we build several generations of a “Larc computer”
Everyday language describing the problem
Problem solution stated formally as an algorithm
Algorithm implemented as a
program
Program executed on a given machine architecture (ISA)
ISA is implemented by a microarchitecture
Each element of the microarchitecture is made up of logic circuits
Each logic circuit is made up of electronic devices

## Slide 36: Architecture versus Organization
What’s the difference?

## Slide 37: Architecture
Computer Architecture, as in Instruction Set Architecture (or ISA), includes all of the features of the system that are visible to the machine language programmer and that have a direct impact on the logical execution of programs:
Instruction set, register set, number of bits used for data representation, I/O mechanisms, addressing modes
Relevant question: Is there a “multiply” instruction?

## Slide 38: Organization
Computer Organization deals with the way that the features of the architecture are implemented, i.e., the operational units of the computer system and their interconnections:
ALU, register file, control signals, memory organization, interfaces, instruction-level parallelism (e.g., pipeline, superscalar units)
Relevant question: Is there a hardware multiplication unit or is it done in software (e.g., using algorithms such as shift-and-add or Booth)?

## Slide 39: Why study computer organization?
Studying computer organization will help you:
if you end up working at Intel, AMD, ARM Holdings, etc.
if you want to understand the most important tool at the heart of computing
if you care about the performance of your programs
if you decide to work in the areas of programming languages, compilers, databases, operating systems or networking
if you are ever in charge of selecting the most cost-effective hardware for a given computing environment
if you develop software for embedded systems

## Slide 40: Performance metrics for computers
Which criteria would you use when selecting a computer?
???

## Slide 41: Defining performance
Not so easy.

## Slide 42: Some performance metrics
Response time (or execution time or latency)?
  Who cares?
  How to compute it?
Throughput (or bandwidth)
  Who cares?
  How to compute it?

## Slide 43: True or false?
Replacing a processor with a faster one will improve response time.
Replacing a processor with a faster one will improve throughput.
Adding an identical processor to an existing multi-processor system will improve response time.
Adding an identical processor to an existing multi-processor system will improve throughput.
Conclusion: decreasing response time almost always leads to increasing throughput.

## Slide 44: Performance as execution time
From now on, we focus on execution time.
To increase / decrease performance, we must increase / decrease execution time
In mathematical terms, performance is the ??? of execution time
  One goes up if and only if the other goes down

## Slide 45: Relative performance of two computers
What mathematical formula expresses the fact that computer C1 is n times as fast as (or, equivalently, n times faster than) computer C2?
PerformanceC1 / PerformanceC2 = Execution timeC2 / Execution timeC1 = n
Example: If C2 executes a given program in 12 seconds and C2 is 3.5 times slower than C1, how long will C1 take to execute the same program?
  Use the relative performance equation to justify your answer.

## Slide 46: Watch out!
Watch out for the terminology:
“improve performance”
versus
“improve execution time”

## Slide 47: Measuring performance
Execution time is THE measure of computing performance
In what units should we measure it?
Exactly what should we measure?
  Response time (or elapsed time or wall clock time)
    I.e., total time to complete a task
  CPU execution time
    User CPU time
    System CPU time

## Slide 48: Focus on CPU performance
We’ll distinguish between:
  System performance (elapsed time)
  CPU performance (user CPU time)
We will focus on user CPU performance

## Slide 49: System clock
In what units is the clock cycle measured?
What is the clock speed (clock rate), and how does it relate to clock cycle?
Quartz
crystal
Analog to digital conversion
voltage
time
Clock cycle
Falling edge
Rising edge