## Slide 1: Comp Sci 310
Day 3

## Slide 2: Announcements
Quiz 1 this Friday
Assignment 0 due before class this Friday
  Must be typed

## Slide 3: Impact of design strategies on user experience
Users and designers think about computer performance in different ways, e.g., in seconds versus number of clock cycles.
Let’s relate these two metrics: CPU execution time for a program = # CPU clock cycles for a program * clock cycle time
Or: CPU execution time for a program = # CPU clock cycles / clock rate

## Slide 4: Trade-off
The designer often faces a trade-off between the number of clock cycles needed for a program and the length of each cycle
Why?
Example: Perhaps you reduce the number of clock cycles needed but, in each clock cycle, you need to do more work, thus increasing the length of each cycle

## Slide 5: Example #1
Assume program P runs in 10 seconds on computer A clocked at 2GHz.
Let us design and build a new computer B that will run this program in 6 seconds.
What is the RELATIVE performance increase?
What is the performance increase as a PERCENTAGE of A’s execution time?
Now, we know that the clock rate can be increased significantly, but we also realize that the new design will affect the rest of the CPU in such a way that computer B will need 20 percent more clock cycles than A to run the same program P.
What should the clock rate of computer B be to achieve the runtime of 6 seconds for P?

## Slide 6: Recap
We measure performance as CPU execution time per program
The factors that influence this performance metric are:
  The number of clock cycles needed to execute the program, and
  The duration of each clock cycle
But, something is missing…

## Slide 7: So far
So far, we have put ourselves in the shoes of a user and system designer
As a software developer, when you study a program to estimate its efficiency, what is the most important feature of the program in your analysis?
  “In between” elapsed time and clock cycles

## Slide 8: Two basic facts
The execution time of a program is equal to the number of instructions executed times the time it takes to execute an instruction (in clock cycles)
Some instructions take longer to execute than others.

## Slide 9: Instruction performance
The execution time of a program is equal to the number of instructions executed by the program, called the instruction count (IC), multiplied by the average time it takes to execute an instruction.
New parameter: CPI = average number of clock cycles per instruction
The CPI provides one way of comparing two different implementations of the same ISA.

## Slide 10: Example #2
Suppose computers A and B implement the same ISA.
Computer A has a clock cycle time of 250ps and a CPI of 2.0 for some program P.
Computer B has a clock cycle time of 500ps and a CPI of 1.2 for the same program P.
Which computer is faster for P and by how much?

## Slide 11: “Classic” CPU performance equation
CPU execution time for a program = IC * CPI * Clock cycle time
Equivalently: CPU execution time for a program = IC * CPI * 1/Clock rate
These equations are important because they identify the three factors that affect CPU performance.

## Slide 12: Example #3
A compiler writer must generate machine code for a particular high-level language statement. The choice is between two machine code sequences with the following instruction counts:
The hardware designers have supplied the following facts:
Which code sequence executes the most instructions?
Which code sequence will be faster?
What is the CPI for each code sequence?
Code sequence
A
IC for each instruction class
B
C
1
2
2
1
2
1
1
4
A
CPI for each instruction class
B
C
CPI
1
2
3

## Slide 13: Summary
CPU execution time for a program = # instructions for a program * # clock cycles / instruction * seconds / clock cycle
Equivalently: CPU execution time = IC * CPI * clock cycle time
Equivalently: CPU execution time = IC * IPC * 1 / clock rate
Component
Units of measure
CPU execution time for a program P
Number of seconds taken by CPU to execute P
IC
Number of instructions executed by P
CPI
Average number of clock cycles per instruction in P
Clock cycle time
Seconds per clock cycle

## Slide 14: Things to think about
What is the smallest possible value of CPI?
Definition: IPC, or # of instructions per clock cycle

## Slide 15: Last example
Suppose program P runs in 100 seconds on a computer
Multiply operations account for 80 seconds of this time
How much do you have to improve the speed of multiplication if I want my program to run 5 times faster (i.e., in 20 seconds)?

## Slide 16: Multiplication 10 times faster
What if multiplication is 10 times faster?
New execution time:
  Total execution time: 100 total seconds
    80 seconds of multiplication
      Multiplication is NOW 10 times as fast…
        Result: 8 seconds of multiplication
          Plus 20 seconds of non-multiplication
            Total: 20 + 8 = 28 seconds
              28 seconds
                NOT 5 times as fast (28 > 20)

## Slide 17: Another approach
Execution time after improvement = Execution time affected by improvement / improvement factor + Execution time unaffected.
For this problem: 20 = 80 seconds / x + (100 – 80 seconds)  0 = 80 seconds / x  x = ???
5x improvement not possible in this case!

## Slide 18: Amdahl’s law
The overall system performance increase due to a speedup factor of x in one component of the system is limited by the fraction of time that this component is used by the system
Gene Amdahl
  PhD UW—Madison (theoretical physics)