## Slide 1: Comp Sci 310
Day 4

## Slide 2: Announcements
Quiz 1 this Friday (9/12)
Assignment 0 due on Friday
  BEFORE the start of class
Quiz 2 on Monday (9/15)
Assignment 1 posted tonight on d2l
  Due: BEFORE the start of class on 9/19
  Must work with a partner on all assignments > 0
    Same partner for the entire semester

## Slide 3: Warm-up example
Consider the following measurements for two different processors P1 and P2 and a given program P:
CR_____ IC____ time
P1 : 2 Ghz 6 * 109 4 s
P2 : 1.5 Ghz 2 * 109 9 s
What is the clock rate for P2 that would give P2 the same CPI as P1?

## Slide 4: Computers as complex systems
In general, complex systems are built out of many interconnected parts and possibly other sub-systems.
Functions of a computer:
  Data processing
  Data storage
  Data movement
  Control
Structure of a computer:
  I.e., computer organization
  Hierarchy of levels

## Slide 5: Hierarchical organization
Computer System:
Memory
I/O devices
Interconnect (system bus, etc.)
Processor (or CPU)
  ALU
  Registers
  Internal bus
  Control unit
    Control memory
    Microinstruction sequencing logic
    Registers, decoders
COMPUTER
MAIN MEMORY
I/O
SYSTEM
BUS
CPU
CPU
REGISTERS
Internal
BUS
Control
unit
ALU
Sequencing
logic
Control unit registers and decoders
Control
memory
Control
Unit

## Slide 6: The digital computer
The operation of the digital computer is based on the storage and processing of binary data
Computers are built out of storage elements that can exist in one of two stable states and or circuits that can operate on binary data
We will now focus on how to implement these digital circuits…

## Slide 7: Boolean algebra
Boolean algebra is the mathematical foundation of digital logic. It is a model that is convenient for:
Analysis: It is an economical way of describing the function of digital circuitry
Design: Given a desired function, Boolean algebra can be applied to develop a simplified implementation of that function

## Slide 8: Boolean variables
As with any algebra, Boolean algebra makes use of variables and operations
Logical variables
Logical operations
A variable may take on the value 1 (TRUE) or 0 (FALSE)
E.g., D = A V ( ¬B Λ C )
  Meaning: D is equal to 1 if A is 1 or both B = 0 and C = 1. Otherwise, D is 0.

## Slide 9: Boolean operators
These should be a review:
The above operations can be generalized to more than two inputs.
P | Q | NOT P ¬P | P AND Q P Λ Q | P OR Q P V Q | P NAND Q ¬(P Λ Q) | P NOR Q ¬(P V Q) | P XOR Q (P Λ ¬Q) V (¬P Λ Q)
0 | 0 | 1 | 0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0

## Slide 10: Boolean identities
Basic Postulates:
A Λ B = B Λ A A V B = B V A Commutative Laws
A Λ (B V C) = (A Λ B) V (A Λ C) A V (B Λ C) = (A V B) Λ (A V C) Distributive Laws
1 Λ A = A 0 V A = A Identity Elements
A Λ ¬A = 0 A V ¬A = 1 Inverse Elements
Other identities:
0 Λ A = 0 1 V A = 1
A Λ A = A A V A = A
A Λ (B Λ C) = (A Λ B) Λ C A V (B V C) = (A V B) V C Associative Laws
¬(A Λ B) = ¬A V ¬B ¬(A V B) = ¬A Λ ¬B DeMorgan’s Theorem

## Slide 11: Logic gates
AND
A
B
F
F = A Λ B
A
B
F
0
0
0
0
1
0
1
0
0
1
1
1
OR
A
B
F
F = A V B
A
B
F
0
0
0
0
1
1
1
0
1
1
1
1
NOT
A
F
F = ¬A
A
F
0
1
1
0
NAND
A
B
F
F = ¬ (A Λ B)
A
B
F
0
0
1
0
1
1
1
0
1
1
1
0
NOR
A
B
F
F = ¬(A V B)
A
B
F
0
0
1
0
1
0
1
0
0
1
1
0
XOR
A
B
F
F = A XOR B
A
B
F
0
0
0
0
1
1
1
0
1
1
1
0

## Slide 12: Logically universal set of gates
Not all gate types are needed in implementation
Design and fabrication are simpler if only one or two types of gates are used
Thus, it is important to identify functionally universal sets of gates
  Meaning: any Boolean function can be implemented using only the gates in the set

## Slide 13: Universally complete sets
And, Or, Not
And, Not (?)
Or, Not (?)
Nor (?)
Nand (?)

## Slide 14: Examples
Make Not, And and Or out of just Nand gates.
DeMorgan’s Theorem: A V B = ¬(¬(A V B)) = ¬(¬A Λ ¬B) =
¬(¬A) V ¬(¬B) = A V B.
A
¬A
A
B
¬(A Λ B)
A Λ B
A
B
A V B

## Slide 15: Digital circuits
Computers are built from two kinds of digital circuits:
Combinational circuit:
  The outputs are a Boolean combination of its current inputs only
  Same inputs always produce the same outputs
  The outputs constantly track the inputs (after a propagation delay)
Sequential circuit:
  The outputs depend not only on the current inputs, but also on the history of the inputs
  Contains memory elements (e.g., D flip-flop) that remember the state of the system
  Think of a garage door opener
  Usually synchronous, i.e., clocked.
D
C
Q

## Slide 16: Combinational circuits needed for our first Larc computer
Out of Nand gates ONLY, we need to build the following gates and circuits:
Unary gate: Not
Binary gates:
  And
  Or
  Xor
Circuits:
  A variety of multiplexers
  A variety of demultiplexers
  A full 1 bit-adder
  A 1-bit ALU
  A 16-bit ALU
  A 16-bit parallel adder
  A 16-bit increment-by-one circuit

## Slide 17: Hardware description languages
These days, most digital design of processors is done using a hardware description language (HDL)
Enables the designer to work with a text description of the hardware
  As opposed to schematics
Goals of an HDL are to help designer:
  debug using a simulator
  Compile their design into hardware implementation

## Slide 18: In this course
We will use a simple HDL that comes with a simulator so we can design and test our Larc computers
To reach this goal, we will first build simple chips (e.g., basic gates)
Then combine them into more complex chips, including a Larc CPU and RAM.

## Slide 19: Chip definition in HDL: Interface
The chip’s architect is responsible for providing the chip’s interface (similar to a contract or API), including:
Chip name
Name of its input and output pins
Documentation of intended chip operation

## Slide 20: Example
The interface is given to you in a text file called <chip_name>.hdl, such as:
/**
* Not gate: out = not(in)
*/
CHIP Not { // uppercase words are keywords
IN in; // only one input pin
OUT out; // only one output pin
PARTS: // beginning of implementation section
// implementation missing
}

## Slide 21: A lot of chips
In the upcoming assignments, you will have to implement a lot of chips
Implementation boils down to:
  Choosing appropriate components, e.g., built-in gates (the Nand gate) or other chips
  Wiring the parts correctly

## Slide 22: Chip definition in HDL: implementation
The implementation of the chip goes into the last part of the <chip_name>.hdl file
May only use chips that have been previously built
  Made clear from the assignment handouts
You will be responsible for building each chip as economically as possible
/* Not gate: out = not(in) */
CHIP Not { // uppercase words are keywords
IN in; // only one input pin
OUT out; // only one output pin
PARTS:
Nand(a=in, b=in, out=out); // only one internal part in this chip
}