## Slide 1: Comp Sci 310
Day 5

## Slide 2: Announcements
Quiz 2 on Monday (9/15)
Assignment 1 posted on d2l
  Due: BEFORE the start of class on 9/19
  Must work with a partner on all assignments > 0
    Same partner for the entire semester
Quiz 3 on Friday (9/19)
  Maybe (depending on how much we cover in class)

## Slide 3: Warm-up example
Let F be a boolean function.
We know that F can be represented with a corresponding truth table
Implement this boolean function using logic gates:
x | y | z | F(x,y,z)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 4: Warm-up solution
x | y | z | F(x,y,z)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
F(x,y,z) =
(¬x Λ y Λ z)
V
(x Λ ¬y Λ ¬z)
V
(x Λ y Λ ¬z)
V
(x Λ y Λ z)

## Slide 5: With gates
F(x,y,z) = (¬x Λ y Λ z) V (x Λ ¬y Λ ¬z) V (x Λ y Λ ¬z) V (x Λ y Λ z)
Minimize this for fun!
F(x,y,z)

## Slide 6: Built-in Nand: interface
The implementation of the chip goes into the last part of the <chip_name>.hdl file
May only use chips that have been previously built
  Made clear from the assignment handouts
Try to build each chip as economically as possible
/* Nand gate: out = a NAND b */
CHIP Nand {
IN a, b; // two input pins
OUT out; // only one output pin
PARTS:
BUILTIN Nand; // Because of the BUILTIN keyword, you do not
// have to implement this gate.
}
Now, let’s get started on the next assignment (assignment 2) and build the other gates we need

## Slide 7: Implementation of the Not gate
/* Not gate: out = not(in) */
CHIP Not { // uppercase words are keywords
IN in; // only one input pin
OUT out; // only one output pin
PARTS:
Nand(a=in, b=in, out=out); // only one internal part in this chip
}

## Slide 8: Implementation of the And gate
/* And gate: out = a AND b */
CHIP And {
IN a, b;
OUT out;
PARTS:
// Implementation missing
}
Which parts will you need?
How will you wire them?

## Slide 9: Implementation of the And gate: hdl file
/* And gate: out = a AND b */
CHIP And {
IN a, b;
OUT out;
PARTS:
Nand(a=a, b=b, out=out1);
Nand(a=out1, b=out1, out=out);
}
A
B
¬(A Λ B)
A Λ B

## Slide 10: Implementation of the Or gate
/* Or gate: out = a OR b */
CHIP Or {
IN a, b;
OUT out;
PARTS:
// Implementation missing
}
Which parts will you need?
How will you wire them?
You will also have to build an Or16Way gate with 16 inputs

## Slide 11: Implementation of the Xor gate
/* Xor gate: out = a XOR b */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
// Implementation missing
}
Which parts will you need?
How will you wire them?

## Slide 12: Hardware Simulator
Run HardwareSimulator.bat
  Can also run HardwareSimulator.sh from your Linux account: type: ./HardwareSimulator.sh &
Read Part 1 of the Hardware Simulator Tutorial manual
Test the previous examples