## Slide 1: Comp Sci 310
Day 6

## Slide 2: Announcements
Assignment 1 due BEFORE the start of class on 9/19
  Show your work / reasoning
  Type your solutions for credit
Quiz 3 on Friday (9/19)
  Maybe (depending on how much we cover in class)

## Slide 3: Warm-up
Give the hdl code that specifies a chip that always outputs zero.

## Slide 4: Multiplexers
A multiplexer is a digital circuit whose output is selected from a set of 2n input signals
At any time, exactly one of the input data signals is chosen and simply forwarded to the output pin
Chosen input data signal depends on the value of n input control signals or selection signals

## Slide 5: Example: 2-to-1 multiplexer (n = 1)
D0
D1
S0
0
1
O
D0 | D1 | S0 | O
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
S0 | O
0 | ??
1 | ??
Mux schematic:
Mux summary truth table:
Mux truth table:
S0 | O
0 | D0
1 | D1
What is the Boolean formula for O?
(D0 V S0) Λ (D1 V ¬S0)

## Slide 6: Example
Give the hdl code for (2-to-1) Mux

## Slide 7: Example: 4-to-1 multiplexer (n = 2)
D0
D1
S1
0
1
O
Mux schematic:
Mux summary truth table:
Mux truth table:
D2
D3
2
3
S0
How many rows would there be in this truth table?
26
S1 | S0 | O
0 | 0 | D0
0 | 1 | D1
1 | 0 | D2
1 | 1 | D3

## Slide 8: More multiplexers
If there are n values to choose from, you must use an n-way multiplexer
How would you use Mux to build Mux4Way?
How would you use Mux4Way to build Mux8Way?
D0
D1
S0
0
1
O
D0
D1
S1
0
1
O
D2
D3
2
3
S0

## Slide 9: Mux4Way from Mux
D0
D1
0
1
D0
D1
S1
0
1
O
D2
D3
2
3
S0
S1 | S0 | O
0 | 0 | D0
0 | 1 | D1
1 | 0 | D2
1 | 1 | D3
D2
D3
0
1
S1
S0
0
1
D0 / D1
D2 / D3

## Slide 10: Mux8Way from Mux4Way
Use two Mux4Ways and one Mux.

## Slide 11: Multi-bit multiplexers
In Larc: registers are 16 bits wide
  E.g., the program counter (PC) contains a single 16-bit address
PC is modified during every fetch-execute cycle
New value computed differently based on the current instruction
PC incremented by 1 for ALU ops
  computed using an offset otherwise
Compute BOTH and use a multiplexer to select appropriate new input based on current opcode (select signal)
Main difference: each input is wider than 1 bit

## Slide 12: Mux16
Here are the schematic and truth table for the 2-to-1 16-bit wide multiplexer:
D0
D1
S0
0
1
O
Mux16 truth table:
How many rows would there be in this truth table?
233
16
16
16
Mux summary truth table:
S0 | O
0 | D0
1 | D1
Mux16 schematic:
D0[0] | ... | D0[15] | D1[0] | … | D1[15] | S0 | O

## Slide 13: Additional multi-bit multiplexers
D0
D1
S1
0
1
O
Mux4Way16 schematic:
Mux4Way16 summary truth table:
Mux4Way16
truth table:
D2
D3
2
3
S0
How many rows would there be in this truth table?
24*16+2 = 266
S1 | S0 | O
0 | 0 | D0
0 | 1 | D1
1 | 0 | D2
1 | 1 | D3
Here are the schematic and truth table for the 4-to-1 16-bit wide multiplexer:
16
16
16
16
16
How would you define the interface of a Mux8Way16 multiplexer? How would you implement it?
How would you define the interface of a Mux16Way16 multiplexer? How would you implement it?

## Slide 14: Mux8Way16 interface
/* Mux8Way16 */
CHIP Mux8Way16{
IN i0[16], // 16-bit inputs
i1[16],
i2[16],
i3[16],
i4[16],
i5[16],
i6[16],
i7[16]; // 8 of them
OUT out;
PARTS:
// Implementation missing
}

## Slide 15: Mux8Way16
Think about how we built the Mux4Way.
That is, use two Mux4Way16s and one Mux16.