## Slide 1: Comp Sci 310
Day 7

## Slide 2: Announcements
Assignment 1 due BEFORE the start of class on MONDAY, 9/22
  Show your work / reasoning
  Type your solutions for credit
Quiz 3 on Friday (9/19)
  Multiplexers, demultiplexers, etc.
Assignment 2 posted on d2l sometime on Friday 9/19

## Slide 3: Demultiplexers
A demultiplexer is a digital circuit with 2n output signals
Exactly one of which is selected to forward the unique input
  The other outputs are all 0
The selected output signal depends on the value of the n input control (selection) signals

## Slide 4: Example: 1-to-2 demultiplexer (n = 1)
I
O0
O1
S0
I | S0 | O0 | O1
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
S0 | O0 | O1
0 | I | 0
1 | 0 | I
DMux schematic:
DMux summary truth table:
DMux truth table:
0
1
How would you build a Dmux?
How would a DMux4Way behave and how would you build it?
How about a DMux8Way?
A DMux16Way?

## Slide 5: Building the DMux
I
O0
O1
S0
0
1
O0 = I Λ ¬S0
O1 = I Λ S0
You can easily build these circuits (using just Nand gates)!

## Slide 6: Building a DMux4Way
I
S1
0
1
O0
2
3
S0
O1
O2
O3
I
S1
0
1
S1 | S0 | O0 | O1 | O2 | O3
0 | 0 | I | 0 | 0 | 0
0 | 1 | 0 | I | 0 | 0
1 | 0 | 0 | 0 | I | 0
1 | 1 | 0 | 0 | 0 | I
0
1
0
1
O0
O1
O2
O3
S0

## Slide 7: Arithmetic
The basic arithmetic operations can be carried out using only Boolean algebra
For the addition of two bits, one new feature is the possible generation of a carry bit
The carry bit must be fed into the next two-bit addition (in sequence)

## Slide 8: Truth tables for addition
How would you implement the carry (COUT) bit?
How would you implement the sum bit without using the following gates: Not, And, Or?
Single-bit addition |  |  | 
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Addition with Carry Input |  |  |  | 
CIN | A | B | Sum | COUT
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 9: Single-bit addition: half adder
B
A
S
C

## Slide 10: Addition with carry input: full adder
B
A
S
COUT
CIN
Can you make a full adder with two half adders?

## Slide 11: A full adder from half adders
B
A
S
C
B
A
S
C
CIN
COUT

## Slide 12: Multiple-bit addition and subtraction
How to implement subtraction
  Recall that: A – B = ???
A parallel adder can be used to perform both n-bit additions and n-bit subtractions
B0
A0
S0
0
CIN
C0
B1
A1
S1
CIN
C1
B2
A2
S2
CIN
C2
B3
A3
S3
CIN
C3
Overflow signal

## Slide 13: Larc ISA
All memory words are 16-bit words
Each address is 16 bits long
  What is the address space?
Each instruction is 16 bits long
There are 16 user-visible registers
See also: Section 3.4 in the Larc manual

## Slide 14: Warm-up: 1 bit ALU
For now, we only implement 3 of the ALU operations:
  add, sub, nor
This chip will need ??? control signals to choose one of the three possible operations
  ??? = 2

## Slide 15: 1-bit ALU interface
/** A one-bit ALU: out = a <op> b (with carry-in and carry-out for
* add/sub only)
*
* if (sub == nor == 0) then cout = COUT(FA(cin, a, b))
* out = SUM(FA(cin, a, b))
* else if (sub == 1 && nor == 0) then cout = COUT(FA(cin, a, !b))
* out = SUM(FA(cin, a, !b))
* else /* nor == 1 */ out = a NOR b
*/
CHIP ALU1bit {
IN a,b, // the two one-bit inputs
cin, // the carry-in bit (needed for add/sub)
sub, // 1 if subtraction is the operation to compute
nor; // 1 if NOR is the operation to compute
OUT out, // the one-bit output
cout; // the carry-out bit (needed for add/sub)
PARTS:
/* implementation missing */
}

## Slide 16: 1-bit ALU implementation
b
a
FULL ADDER
cout
sum
cin
0
1
sub
b
a
cin
nor
cout
out

## Slide 17: 16-bit ALU (without SLT)
/** 16-bit ALU: out = a <op> b, where <op> is defined as follows:
*
* if (sub == nor == 0) then out = a + b (z set if out == 0)
* else if (sub == 1 && nor == 0) then out = a - b
* (z set if out == 0)
* else /* nor == 1 */ out = a NOR b (z set if out == 0)
*/
CHIP ALU {
IN a[16], b[16], // the two 16-bit inputs
sub, // 1 if subtraction is the operation to compute
nor; // 1 if NOR is the operation to compute
OUT out[16], // the 16-bit output
z; // 1 if out is equal to 0
PARTS:
/* implementation missing */
}

## Slide 18: Implementation of 16-bit ALU
sub
b
a
cin
nor
1-bit ALU
Bit 15 (MSB)
out
cout
nor
b
a
sub
16
16
1
1
sub
b
a
cin
nor
1-bit ALU
Bit 1 (MSB)
out
cout
1
1
sub
b
a
cin
nor
1-bit ALU
Bit 0 (MSB)
out
cout
1
1
1
1
1
1
1
@
1
16
out
z