## Slide 1: Comp Sci 310
Day 8

## Slide 2: Announcements
Quiz 4 on Monday (9/22)
  Binary addition, adders, etc.

## Slide 3: Truth tables for addition
How would you implement the carry (COUT) bit?
How would you implement the sum bit without using the following gates: Not, And, Or?
Single-bit addition |  |  | 
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Addition with Carry Input |  |  |  | 
CIN | A | B | Sum | COUT
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 4: 1-bit ALU interface
/** A one-bit ALU: out = a <op> b (with carry-in and carry-out for
* add/sub only)
*
* if (sub == nor == 0) then cout = COUT(FA(cin, a, b))
* out = SUM(FA(cin, a, b))
* else if (sub == 1 && nor == 0) then cout = COUT(FA(cin, a, !b))
* out = SUM(FA(cin, a, !b))
* else /* nor == 1 */ out = a NOR b
*/
CHIP ALU1bit {
IN a,b, // the two one-bit inputs
cin, // the carry-in bit (needed for add/sub)
sub, // 1 if subtraction is the operation to compute
nor; // 1 if NOR is the operation to compute
OUT out, // the one-bit output
cout; // the carry-out bit (needed for add/sub)
PARTS:
/* implementation missing */
}

## Slide 5: 16-bit ALU (without SLT)
/** 16-bit ALU: out = a <op> b, where <op> is defined as follows:
*
* if (sub == nor == 0) then out = a + b (z set if out == 0)
* else if (sub == 1 && nor == 0) then out = a - b
* (z set if out == 0)
* else /* nor == 1 */ out = a NOR b (z set if out == 0)
*/
CHIP ALU {
IN a[16], b[16], // the two 16-bit inputs
sub, // 1 if subtraction is the operation to compute
nor; // 1 if NOR is the operation to compute
OUT out[16], // the 16-bit output
z; // 1 if out is equal to 0
PARTS:
/* implementation missing */
}

## Slide 6: Implementation of 16-bit ALU
sub
b
a
cin
nor
1-bit ALU
Bit 15 (MSB)
out
cout
nor
b
a
sub
16
16
1
1
sub
b
a
cin
nor
1-bit ALU
Bit 1
out
cout
1
1
sub
b
a
cin
nor
1-bit ALU
Bit 0 (LSB)
out
cout
1
1
1
1
1
1
1
@
1
16
out
z

## Slide 7: ALU Subtraction example
a=1
b=1
out = SUM(FA(cin, a, ¬b) = SUM(FA(1,1,0)) =
cout = COUT(FA(cin, a, ¬b) = COUT(FA(1,1,0)) =
a=0
b=0
out = SUM(FA(cin, a, ¬b,) = SUM(FA(1,0,1)) =
cout = COUT(FA(cin, a, ¬b) = COUT(FA(1,0,1)) =
a
b
1
1
0
0
1
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
MSB
LSB
a=1
b=0
out = SUM(FA(cin, a, ¬b,) = SUM(FA(1,1,1)) =
cout = COUT(FA(cin, a, ¬b) = COUT(FA(1,1,1)) =
a=0
b=1
out = SUM(FA(cin, a, ¬b,) = SUM(FA(1,0,0)) =
cout = COUT(FA(cin, a, ¬b) = COUT(FA(1,0,0)) =
cin=1
cin=1
cin=1
cin=1
-4
0
1
0
1
1
1
1
0

## Slide 8: 16-bit ALU (with SLT)
/** 16-bit ALU: out = a <op> b, where <op> is defined as follows:
*
* if (sub == nor == 0) then out = a + b (z set if out == 0)
* else if (sub == 1 && nor == 0) then out = a - b
* (z set if out == 0)
* else if (sub == 0 && nor == 1) then out = a NOR b * (z set if out == 0)
* else /* sub == nor == 1 */ out = 1 iff a < b (z is undefined)
*/
CHIP ALU {
IN a[16], b[16], // the two 16-bit inputs
sub, // 1 if subtraction is the operation to compute
nor; // 1 if NOR is the operation to compute
OUT out[16], // the 16-bit output
z; // 1 if out is equal to 0
PARTS:
/* implementation missing */
}

## Slide 9: Any ideas?
How should we modify the 16-bit ALU (without SLT) to support SLT?
Key observation: a < b iff a - b < 0
What does the bit pattern of a - b look like, assuming a < b?
  Hint: negative values in two’s complement have leading 1’s.

## Slide 10: Implementation of 16-bit ALU with SLT
sub
b
a
cin
nor
1-bit ALU
Bit 15 (MSB)
out
cout
nor
sub
16
16
1
1
sub
b
a
cin
nor
1-bit ALU
Bit 1
out
cout
1
1
sub
b
a
cin
nor
1-bit ALU
Bit 0 (LSB)
out
cout
1
1
1
1
1
1
1
@
1
16
out
z
1
15
b
a

## Slide 11: Implementation of 16-bit ALU with SLT
sub
b
a
cin
nor
1-bit ALU
Bit 15 (MSB)
out
cout
nor
sub
16
16
1
1
sub
b
a
cin
nor
1-bit ALU
Bit 1
out
cout
1
1
sub
b
a
cin
nor
1-bit ALU
Bit 0 (LSB)
out
cout
1
1
1
1
1
1
1
@
1
16
out
z
1
15
b
a

## Slide 12: Implementation of 16-bit ALU with SLT
sub
b
a
cin
nor
1-bit ALU
Bit 15 (MSB)
out
cout
nor
sub
16
16
1
1
sub
b
a
cin
nor
1-bit ALU
Bit 1
out
cout
1
1
sub
b
a
cin
nor
1-bit ALU
Bit 0 (LSB)
out
cout
1
1
1
1
1
1
1
@
1
16
out
z
16
@
00…00
1
15
b
a

## Slide 13: Implementation of 16-bit ALU with SLT
sub
b
a
cin
nor
1-bit ALU
Bit 15 (MSB)
out
cout
nor
sub
16
16
1
1
sub
b
a
cin
nor
1-bit ALU
Bit 1
out
cout
1
1
sub
b
a
cin
nor
1-bit ALU
Bit 0 (LSB)
out
cout
1
1
1
1
1
1
1
@
1
16
out
z
16
0
1
@
16
00…00
1
15
b
a

## Slide 14: Implementation of 16-bit ALU with SLT
sub
b
a
cin
nor
1-bit ALU
Bit 15 (MSB)
out
cout
nor
sub
16
16
1
1
sub
b
a
cin
nor
1-bit ALU
Bit 1
out
cout
1
1
sub
b
a
cin
nor
1-bit ALU
Bit 0 (LSB)
out
cout
1
1
1
1
1
1
1
@
1
16
out
z
16
0
1
@
16
00…00
1
15
b
a