## Slide 1: Comp Sci 310
Day 9

## Slide 2: Announcements
Quiz 5 on Monday, 9/29
Assignment 2 is posted on d2l
  Due on Wednesday, 10/1
Interested in a study group?
  Contact Brian Zimmerman

## Slide 3: We need memory
All of the circuits we have built so far compute new values from old ones
  This is what combinational circuits do
Computer systems also need to store values for later use!
How do we build storage elements using only Nand gates?

## Slide 4: Digital circuits
Computers are built from two kinds of digital circuits:
Combinational circuit:
  The outputs are a Boolean combination of its current inputs only
  Same inputs always produce the same outputs
  The outputs constantly track the inputs (after a propagation delay)
Sequential circuit:
  The outputs depend not only on the current inputs, but also on the history of the inputs
  Contains memory elements (e.g., D flip-flop) that remember the state of the system
  Think of a garage door opener
  Usually synchronous, i.e., clocked.
D
Q
QB
RSTB
SET

## Slide 5: Complementarity of combinational and sequential circuits
Without memory or state elements, where would the inputs of combinational circuits come from?
  Where would their outputs go to?
State elements, e.g., registers, memory locations, etc., solve this problem
In general: combinational circuits take their inputs from some sequential circuits and send their outputs to (possibly the same) sequential circuits
Register 1
Register 2
Combinational logic
Clock

## Slide 6: Clocking methodology
Clocking methodology is the scheme used to determine when data is valid and stable, relative to the clock
  I.e., when signals can be read and written
What would happen if a 16-bit value were read at the same time it is written?

## Slide 7: Positive edge-triggered
All of our computer systems will use an edge-triggered clocking methodology
All state changes occur on the same clock edge
Positive edge-triggered methodology: state changes occur on the rising of the clock signal
  Transition from low to high
Register 1
Register 2
Combinational logic
Clock
Rising edge
Falling edge

## Slide 8: Flip-flops
The basic building block for ALL of our sequential circuits will be a flip-flop: the D (for data) flip-flop.
/**
* An edge-triggered D flip-flop: out(t)=in(t-1)
* where t is the current time unit, or clock cycle
*/
CHIP DFF {
IN in; // note that the clock signal is another
// implicit input
OUT out;
BUILTIN DFF;
CLOCKED in; // this chip, and all chips that use it,
// are sequential
}
A D flip-flop outputs the signal from the previous time unit

## Slide 9: Behavior of a positive-edge-triggered D flip-flop
D | Clock | Q(t)
0 | ↑ | 0
1 | ↑ | 1
X | 0 | D(t – 1)
X | 1 | D(t – 1)
Clock
Din
Qout