## Slide 1: Comp Sci 310
Day 20

## Slide 2: Announcements
Assignment 3 due on Monday, 10/27 at 11:59 PM
  Implementation of memory chips
Quiz 8 on Monday, 10/20
  Performance of single-cycle vs. multi-cycle, multiplication, etc.
    Whatever we cover before then
  Exam 2: Friday, 11/7

## Slide 3
PC
IM
address
instruction
RF
DM
RR1
RR2
WR
WD
RD1
RD2
address
RD
WD
0
1
2
3
SIGN EXTEND
<< 8
LIMM
ADD
0..0
[4..11]
0
1
ADD
00..01
SIGN EXTEND
SIGN EXTEND
ALU
z
RC[0..3]
RA[8..11]
LIMM
[0..7]
SIMM[8..11]
SIMM[0..3]
0
1
0
1
0
1
RFWRITE
RFWD
SE
LW
ALU
SUB
NOR
SW
RD1
2
RB[4..7]
BN
BE
0
1
0
1
JAL
CONTROL UNIT
OPCODE[12..15]
Single-cycle Larc implementation

## Slide 4: Single-cycle implementations
What is the CPI for a single-cycle implementation?
Often very inefficient
  Why?
Clock cycle time determined by the longest possible path among all instructions in the ISA
  Must be long enough to execute the “slowest instruction”

## Slide 5: Example
Assume the following operation times for the major functional units:
and the following instruction mix:
What is the relative speedup of a hypothetical variable-length single-cycle implementation over our constant-length single-cycle implementation?
 | Memory unit | ALU and adders | Register file | Muxes, CU, etc.
Operation time | 100 ps | 70 ps | 70 ps | negligible
Load | Store | ALU ops | Cond. Branches | Jumps
15% | 10% | 40% | 20% | 15%

## Slide 6: Solution #1
In single-cycle model, every instruction takes one clock cycle, so the clock cycle must be stretched to accommodate the slowest instruction
Instruction class
Instruction fetch
Register read
ALU op
Data access
Register write
Total time
Load
100 ps
70ps
70 ps
100 ps
70 ps
410 ps
Store
100 ps
70ps
70 ps
100 ps
340 ps
ALU
100 ps
70ps
70 ps
70 ps
310 ps
Branches
100 ps
70ps
70 ps
240 ps
Jumps
100 ps
70ps
70 ps
240ps

## Slide 7: Solution #2
Instruction class
Instruction fetch
Register read
ALU op
Data access
Register write
Total time
Load
100 ps
70ps
70 ps
100 ps
70 ps
410 ps
Store
100 ps
70ps
70 ps
100 ps
340 ps
ALU
100 ps
70ps
70 ps
70 ps
310 ps
Branches
100 ps
70ps
70 ps
240 ps
Jumps
100 ps
70ps
70 ps
240ps
410 ps is our clock cycle time
410 ps
Load | Store | ALU ops | Cond. Branches | Jumps
15% | 10% | 40% | 20% | 15%

## Slide 8: Solution #3
Instruction class
Instruction fetch
Register read
ALU op
Data access
Register write
Total time
Load
100 ps
70ps
70 ps
100 ps
70 ps
410 ps
Store
100 ps
70ps
70 ps
100 ps
340 ps
ALU
100 ps
70ps
70 ps
70 ps
310 ps
Branches
100 ps
70ps
70 ps
240 ps
Jumps
100 ps
70ps
70 ps
240ps
Load | Store | ALU ops | Cond. Branches | Jumps
15% | 10% | 40% | 20% | 15%
410 ps is our clock cycle time
Single-cycle: .15*410 + .1*410 + .4*410 + .2*410 + .15*410 = 410
Variable-cycle: .15*410 + .1*340 + .4*310 + .2*240 + .15*240 =
61.5 + 34 + 124 + 48 +46.5= 314
Relative speedup: 410 / 314 = 1.31…

## Slide 9: Single-cycle design: problems
It is inefficient
  I.e., it has a long clock cycle
Therefore, it breaks a key design principle
  “Make the common case fast”
Some of the functional units must be duplicated
  Which ones?
In summary: single cycle implementation has a low CPI but also a low performance
  And a relatively high hardware cost

## Slide 10: Single-cycle design: solutions
Increase the CPI in order to lower the CCT
Performance of single-cycle implementations is MUCH worse than in our example
  E.g., consider the “multiply” instruction

## Slide 11: Multiplication algorithm (not in 2’s complement)
1011
*1101
-----
1011
0000
1011
1011
--------
10001111

## Slide 12: Multiplication algorithm
1011 <-------- Multiplicand (11)
*1101
-----
1011
0000
1011
1011
--------
10001111

## Slide 13: Multiplication algorithm
1011 <-------- Multiplicand (11)
*1101 <-------- Multiplier (13)
-----
1011
0000
1011
1011
--------
10001111

## Slide 14: Multiplication algorithm
1011 <-------- Multiplicand (11)
*1101 <-------- Multiplier (13)
-----
1011
0000 <------ Partial products
1011
1011
--------
10001111

## Slide 15: Multiplication algorithm
1011 <-------- Multiplicand (11)
*1101 <-------- Multiplier (13)
-----
1011
0000 <------ Partial products
1011
1011
--------
10001111 <-------- Product (143)

## Slide 16: Flowchart for multiplication
Start

## Slide 17: Flowchart for multiplication
1. Test Multiplier0
Start

## Slide 18: Flowchart for multiplication
1. Test Multiplier0
Start
2. Shift the multiplicand register left 1 bit
Multiplier0 = 0

## Slide 19: Flowchart for multiplication
1. Test Multiplier0
Start
1a. Add multiplicand to product and place the result in Product register
2. Shift the multiplicand register left 1 bit
Multiplier0 = 1
Multiplier0 = 0

## Slide 20: Flowchart for multiplication
1. Test Multiplier0
Start
1a. Add multiplicand to product and place the result in Product register
2. Shift the multiplicand register left 1 bit
Multiplier0 = 1
Multiplier0 = 0
How many bits is the Product?

## Slide 21: Flowchart for multiplication
1. Test Multiplier0
Start
1a. Add multiplicand to product and place the result in Product register
2. Shift the multiplicand register left 1 bit
3. Shift the multiplier register right 1 bit
Multiplier0 = 1
Multiplier0 = 0

## Slide 22: Flowchart for multiplication
1. Test Multiplier0
Start
1a. Add multiplicand to product and place the result in Product register
2. Shift the multiplicand register left 1 bit
3. Shift the multiplier register right 1 bit
Nth
repetition?
Multiplier0 = 1
Multiplier0 = 0

## Slide 23: Flowchart for multiplication
1. Test Multiplier0
Start
1a. Add multiplicand to product and place the result in Product register
2. Shift the multiplicand register left 1 bit
3. Shift the multiplier register right 1 bit
Nth repetition?
Done
Multiplier0 = 1
No: < N repetitions
Yes: N repetitions
Multiplier0 = 0

## Slide 24: Flowchart for multiplication
1. Test Multiplier0
Start
1a. Add multiplicand to product and place the result in Product register
2. Shift the multiplicand register left 1 bit
3. Shift the multiplier register right 1 bit
Nth repetition?
Done
Multiplier0 = 1
No: < N repetitions
Yes: N repetitions
Multiplier0 = 0
What is N?

## Slide 25: Multiply example
1000 1111
1000 1111
1000 1111
0011 0111
0011 0111
0011 0111
0000 1011
0000 1011
0000 1011
0000 1011
0000 1011
0000 1011
0000 0000
Product
1011 0000
1011 0000
0101 1000
0101 1000
0101 1000
0010 1100
0010 1100
0010 1100
0001 0110
0001 0110
0001 0110
0000 1011
0000 1011
Multiplicand
0000
0001
0001
0001
0011
0011
0011
0110
0110
0110
1101
1101
1101
Multiplier
1a: 1 Prod = Prod + Mcand
1a: 1  Prod = Prod + Mcand
1a: 0  No operation
3: Shift right Multiplier
2: Shift left Multiplicand
1a: 1  Prod = Prod + Mcand
Initial values
Step
4
3
2
1
0
Iteration
Multiplicand = 1011, Multiplier = 1101
3: Shift right Multiplier
2: Shift left Multiplicand
3: Shift right Multiplier
2: Shift left Multiplicand
3: Shift right Multiplier
2: Shift left Multiplicand

## Slide 26: Think about it...
The previous multiplication algorithm does not work with 2’s complement numbers
  Do an example on your own
How would you modify it so that it does work for 2’s complement numbers?
We will see better ways to do multiplication later

## Slide 27: Instruction execution times
Problem: instructions in a given ISA have vastly different execution times
Should not adjust clock cycle to handle longest instruction
Solutions:
  Devote a single, varying-length clock cycle to each instruction
  Devote a varying number of constant-length clock cycles to each instruction

## Slide 28: Instruction execution times
Problem: instructions in a given ISA have vastly different execution times
Should not adjust clock cycle to handle longest instruction
Solutions:
  Devote a single, varying-length clock cycle to each instruction
  Devote a varying number of constant-length clock cycles to each instruction

## Slide 29: Multicycle vs. single-cycle microarchitectures
Recall how the execution of each instruction can be broken down into phases:
  Fetch, decode, execute, memory access, write back, etc.
In a multicycle implementation, we devote one clock cycle to each phase

## Slide 30: As a result
One clock cycle for each phase gives us:
Instructions that need few phases execute faster than instructions that need more phases
The clock cycle time of a multicycle microarchitecture is smaller / larger than that of a single-cycle microarchitecture
  Smaller
The CPI of a multicycle microarchitecture is smaller / larger than that of the a single-cycle microarchitecture
  Larger
Multicycle microarchitectures exhibit higher / lower performance than single-cycle microarchitectures
  Higher
    ???

## Slide 31: Clock cycle
We will choose the smallest clock cycle time that will accommodate at most one of the following operations:
  One memory access (load or store)
  One register file access
    Two reads, or one write
  One ALU operation
We choose the clock cycle to be “just barely” long enough to allow information to get from the beginning of one cycle to the end

## Slide 32: Last example
Assume the following operation times for the major functional units:
and the following instruction mix:
What is the relative speedup of the multicycle implementation over our constant-length single-cycle implementation?
 | Memory unit | ALU and adders | Register file | Muxes, CU, etc.
Operation time | 100 ps | 70 ps | 70 ps | negligible
Load | Store | ALU ops | Cond. Branches | Jumps
15% | 10% | 40% | 20% | 15%

## Slide 33: Last solution
Instruction class
Instruction fetch
Register read
ALU op
Data access
Register write
Total cycles
Load
100 ps
70 ps
70 ps
100 ps
70 ps
5
Store
100 ps
70 ps
70 ps
100 ps
4
ALU
100 ps
70 ps
70 ps
70 ps
4
Branches
100 ps
70 ps
70 ps
3
Jumps
100 ps
70 ps
70 ps
3
Load | Store | ALU ops | Cond. Branches | Jumps
15% | 10% | 40% | 20% | 15%
100 ps is our clock cycle time – smallest to accommodate slowest phase.
Single-cycle: .15*410 + .1*410 + .4*410 + .2*410 + .15*410 = 410
Multicycle: .15(5*100) + .1(4*100) + .4(4*100) + .2(3*100) + .15(3*100) =
.15(500) + .1(400) + .4(400) + .2(300) +.15(300) =
75 + 40 + 160 +60 +45 = 115 + 160 + 105 = 380 Relative speedup: 410 / 380 ≈ 1.07
Total time
410 ps
340 ps
310 ps
240 ps
240ps

## Slide 34: Multicycle design: another advantage
Another advantage: a single functional unit may be used multiple times for each instruction
  As long as the unit is used during different clock cycles
IN fact: our new design will have:
  A single ALU
  A single memory unit
    No more separate IM and DM

## Slide 35: Multicycle design: schematic
PC
M
ALU
RF
RR1
RR2
WR
WD
RD1
RD2
address
RD
WD

## Slide 36: Multicycle design: schematic
PC
M
A
L
U
O
u
t
ALU
I
R
R
D
1
RF
RR1
RR2
WR
WD
RD1
RD2
M
D
R
address
RD
WD
R
D
2

## Slide 37: Multicycle design: schematic
PC
M
A
L
U
O
u
t
ALU
I
R
R
D
1
RF
RR1
RR2
WR
WD
RD1
RD2
M
D
R
address
RD
WD
R
D
2